# (a) Calculate the maximum EMF Em and the maximum current Im in the RLC circuit described at right.
The “rms” = root-mean-square value of anything oscillating sinusoidally is its peak value divided by 2.

# (b) Find the magnitude and sign of the phase  by which the driving EMF leads the current.
A negative phase means that the driving EMF lags the current … which is the case here? Does your answer make sense given the reactances you calculated earlier?
# (c) Draw the phasor diagram for this circuit, giving numerical values for the lengths of each phasor (E, VR, VC, VL).
Be sure to draw your diagram carefully: use longer phasors for larger peak voltages.

# (d) What is the resonant frequency 0 of this circuit?
# (e) Calculate the maximum energies UL,max and UC,max stored in the inductor and capacitor.
# (f) Assume that the angular frequency  of the generator is variable. For what  is the total impedance Z equal to 2R? Hint- you will get a quadratic equation.