## Slide 1
Gravitational Physics using
Atom Interferometry
Mark Kasevich
Stanford University

## Slide 2: Light-pulse atom interferometers
2015 laboratory sensor, atomic wavepackets separate by 12 cm before interfering, 1e-13 g resolution after 1 hr.
1991 demonstration of an atom interferometer gravimeter
Atoms imaged in middle of interferometer
Interference at output
2

## Slide 3: Light-pulse atom interferometry
Three contributions to interferometer phase shift:
Propagation shift:
Laser fields (Raman interaction):
Wavepacket separation at detection:
For example, Bongs, App. Phys. B, 2006; with Gen. Rel., Dimopoulos, PRD, 2008.

## Slide 4: Sensitivity for 10 m wavepacket separation
Assumptions:
Wavepackets (Rb) separated by z = 10 m, for T = 1 sec. For 1 g acceleration: Df ~ mgzT/h ~ 1.3x1011 rad
Signal-to-noise for read-out: SNR ~ 105:1 per second.
Resolution to changes in g per shot: dg ~ 1/(Df SNR) ~ 7x10-17 g
106 seconds data collection
Quantum limited accelerometer resolution: ~ 7x10-20 g

## Slide 5: General Relativity/Phase shifts
atom
laser
Light-pulse interferometer phase shifts in GR:
  Geodesic propagation for atoms and light.
  Path integral formulation to obtain quantum phases.
  Atom-field interaction at intersection of laser and atom geodesics.
Prior work, de Broglie interferometry: Post-Newtonian effects of gravity on quantum interferometry, Shigeru Wajima, Masumi Kasai, Toshifumi Futamase, Phys. Rev. D, 55, 1997; Bordé, et al.
Atom and photon geodesics

## Slide 6: Application to Gravitational Wave Detection
J. Hogan, et al., GRG 43, 7 (2011).
P. Graham, et al., arXiv:1206.0818, PRL (2013)
T = 40 s
4e8 m baseline 2 m separation
(no angular averaging of antenna orientation)

## Slide 7
Gravity gradiometer
Gravity gradiometer based on AI.
Used to evaluate system error models (rotation response, laser freq. noise)
Data demonstrating operation of the sensor.
6 generations of instrumentation.

## Slide 8: Insensitivity to laser frequency noise
Graham, et al., arXiv:1206.0818, PRL (2013)
• Long-lived single photon transitions (e.g. clock transition in Sr, Ca, Yb, Hg, etc.).
• Atoms act as clocks, measuring the light travel time across the baseline.
• GWs modulate the laser ranging distance.
Laser noise is common
Excited
state
Enables 2 satellite configurations

## Slide 9: Demonstration apparatus
Ultracold atom source
  ~ 106 at 1 nK
  ~ 105 at 50 pK
Optical Lattice Launch
  13.1 m/s with 2372 photon recoils to 9 m
Atom Interferometry
  2 cm 1/e2 radial waist
  10 W total power
  Dyanamic nrad control of laser angle with precision piezo-actuated stage
Detection
  Spatially-resolved fluorescence imaging
  Two CCD cameras on perpendicular lines of sight
Working to demonstrate h ~ 3e-19/Hz1/2 resolution on ground near 1 Hz.

## Slide 10: Lattice launch
>2000 photon recoils to launch to top of tower.
Momentum transferred in 2 photon recoil increments.

## Slide 11: Ultra-ultra cold atoms
Collimated cloud has inferred effective temperature of <50 picoKelvin
Kovachy, et al., arXiv 1407.6995
Atom cloud refocused to <200 microns (resolution limited) after 2.6 seconds drift.
A lens for atom clouds is realized using a laser beam:
Laser beam profile used in exp’t.
Very low temperatures improve the efficiency of atom/laser interactions by controlling inhomogeneous broadening.

## Slide 12: Large momentum transfer atom optics
Sequences of optical pulses are used to realize large separations between interferometer arms.
Example interferometer
pulse sequence
Position
Time

## Slide 13: Large wavepacket separation
8 cm wavepacket separation
4 cm
LMT demonstration at 2T = 2.3 s
Sequential Raman transitions with long interrogation time.
>98% contrast

## Slide 14: Recent: 12 cm wavepacket separation
Expected contrast from source velocity spread.
20 photon recoil atom optics
Induce offset between interfering wavepackets to observe interference contrast envelope.
Interference Contrast
Offset (microsec)

## Slide 15: Tests of QM: “Macroscopicity”
10 cm
Nimrichter, et al., PRL, 2013
Excluded by present work
We are testing QM at unprecedented energy, length and time scales.
Future work to push this to 1 m length scales
Future exp’t with gold clusters/micromirrors

## Slide 16: Phase shifts
Gravity
Coriolis
Timing asymmetry
Curvature, quantum
Gravity gradient
Wavefront
Tij, gravity gradient
vi, velocity; xi, initial position
g, acceleration due to gravity
T, interrogation time
keff, effective propagation vector
1e10 rad
40 rad

## Slide 17: 2-axis rotation/1 axis acceleration measurement
Interference patterns for rotating platform:
Measurement of rotation rate near null rotation operating point.
Dickerson, et al., arXiv:1305.1700, PRL (2013)
Measurement Geometry
Side view
Top view
2-axis gyroscope

## Slide 18: Ground-based Tests of General Relativity
Schwarzschild metric, PPN expansion:
Corresponding AI phase shifts:
Projected experimental limits:
(Dimopoulos, et al., PRL 2007; PRD 2008)
Just launched:
85Rb at 100 nK (sympathetically and delta-kick cooled)
100K atoms, 100 nK, 2.6 s
Principle of Equivalence
PoE: simultaneously measure phase shifts from 87Rb and 85Rb interferometers.

## Slide 19: Testing Newton’s Law
Sample 8ћk interferometer simulation with T = 1.2 s
Measurement of G
Tests of 1/r2 law
Notes: Since we can think of the laser phase as simply bein

## Slide 20: Stochastic Gravitational Waves (?)
Are there atom configurations which can reach these sensitivity levels?
(Maybe.)

## Slide 21: Collaborators
Experiment:
Jason Hogan
Susannah Dickerson
Alex Sugarbaker
Tim Kovachy
Christine Donnelly
Chris Overstreet
Peter Asenbaum
Theory:
Peter Graham
Savas Dimopoulos
Surjeet Rajendran
Visitors:
Philippe Bouyer (CNRS)
Jan Rudolf (Hannover)
Stanford Funding:
  NASA Fund. Phys.
  NASA NIAC
  Keck Foundation