## Slide 1: Computer Graphics Overview
Color
Displays
Drawing Pipeline

## Slide 2: Color
Light in range 400-780 nm
Tristimulus theory allows color to be reproduced by 3 color components
Subtractive: Cyan, Magenta, Yellow CMY - Used in printing
Additive: Red, Green, Blue -- RGB

## Slide 3: Perception
Eye has light sensitive cells on the retina:
Cones - 3 Types
  “Red”, “Green”, and Blue
Spectral Response Curves
Rods - “monochrome”

## Slide 4: Color Perception

## Slide 5: Additive Color
Additive: Red, Green, Blue -- RGB
Red + Blue + Green light added together = White
Basis of Color LCD
1
2
3
4

## Slide 6: Displays
Color LCD contains rectangular array of colored dots - Pixels
  RGB Triads
  R, G, and B controlled separately per pixel
  8 bits for each R, G and B

## Slide 7: Frame Buffer
Stores image to be refreshed on Display
Dual port: Refresh port + Random-access port
Video RAM
Random-Access port used to load frame buffer with images

## Slide 8: How do we turn on pixels?
We use the Standard Graphics Pipeline
We start with geometric items to draw
Each item is passed down the pipeline to the frame buffer.
  Start with polygons
  End with filled pixels

## Slide 9: Programmer’s Model
Data  Application  Graphics Library  Hardware  Screen
  Data: Info you want to draw
  Application: (Rockets + Asteroids)
  Graphics Library: (Processing, OpenGL)
  Hardware: GPU (ATI / nVidia)
  Screen: GPU’s frame buffer memory

## Slide 10: Drawing Pipeline
Standard drawing process uses a pipeline of computations
Starts with: Collection of polygons
Ends with: Image stored in frame buffer
(Desired result)

## Slide 11: Pipeline
Input device ->
Model traversal ->
Model transform ->
Viewing transform ->
Clipping ->
Project & Map to Viewport ->
Lighting ->
Shading ->
Rasterization -> Display

## Slide 12: Pipeline:Model Traversal
Data structure of Polygons
Each polygon in own coordinate system
List:
0
1
2
3

## Slide 13: Pipeline: Modeling Transform
Move each polygon to its desired location
Operations: Translate, Scale, Rotate
0
1
2
3
x
y

## Slide 14: Pipeline: Viewing Transform
Transform the geometry of the scene into the coordinate space of the camera
  The model truck going up a hill– the camera pans out
x
y

## Slide 15: Clipping
Viewport is area of Frame Buffer where new image is to appear
Clipping eliminates geometry outside the viewport
Viewport
Clipping
Resulting
Polygon

## Slide 16: Rasterization
Find which pixels are covered by polygon:
Plane Sweep: For each polygon
  go line-by-line from min to max
    go from left boundary to right boundary pixel by pixel
      Fill each pixel
2D Process

## Slide 17: Data Representation
2D Objects: (x, y) a 2D Vector
3D Objects: (x, y, z) a 3D Vector
2D Scale: (Sx, Sy) a 2x2 Matrix
2D Rotate (R theta)
2D Translate (Tx, Ty)
Sx 0 2 0 x 4 = 8
0 Sy 0 3 5 15
(
(
)
)
(
(
)
)

## Slide 18: Matrix
A Matrix is a rectangular array of numbers
A single Matrix can be labelled by a single variable
Geometric operations can be represented by a matrix:
  Multiply the matrix times vector to get new vector:
Vnew = M x Vold

## Slide 19: Scale
Sx 0 2 0 x 4 = 2 x 4 + 0 x 5 = 8
0 Sy 0 3 5 0 x 4 + 3 x 5 = 15
(
(
)
)
(
(
)
)
(
)

## Slide 20: 2D Rotation
cos θ -sin θ 0 -1 x 3 = -4
sin θ cos θ 1 0 4 3
(
)
(
(
)
)
x
x
θ

## Slide 21: Homogeneous coordinates
Translate(Tx, Ty, Tz)
  X’ = X + Tx
  Y’ = Y + Ty
  Z’ = Z + Tz
x
y
x
y
x' = x + 3
y' = y + 2

## Slide 22: Homogeneous Coordinates
Add a 4th value to a 3D vector
(x/w, y/w, z/w) <-> (x, y, z, w)
1 | 0 | 0 | Tx |  | X |  | X+Tx
0 | 1 | 0 | Ty | * | Y | = | Y+Tz
0 | 0 | 1 | Tz |  | Z |  | Z+Tz
0 | 0 | 0 | 1 |  | 1 |  | 1

## Slide 23: 3D Graphics

## Slide 24: Project & Map to Viewport
Viewport is area of Frame Buffer where new image is to appear
Projection takes 3D data and flattens it to 2D
Eye
Projection Plane
(Screen)

## Slide 25: Lighting
Simulate effects of light on surface of objects
Each polygon gets some light independent of other objects
Specular
Diffuse (Lambertian)

## Slide 26: Shading
Lighting could be calculated for each pixel, but that’s expensive
Shading is an approximation:
  Gouraud shading: Light each vertex
  Interpolate color across pixels

## Slide 27: Rendering Pipeline
Input device ->
Model traversal ->
Model transform ->
Viewing transform ->
Clipping ->
Project & Map to Viewport ->
Lighting ->
Shading ->
Rasterization -> Display