## Slide 1
IAT 106
Spatial Thinking and Communicating
Auxiliary Views, Cross-sections & SolidWorks Assemblies
Week 6

## Slide 2: Review: Perspective vs. Orthographic Projections
Perspective projectors converge to a finite point while orthographic projectors remain parallel
Perspective
Orthographic
Notes: Remember the folding glass box example?
-The physiology of the human eye causes parallel edges or features to appear to converge at a distance.
-In orthographic views, projectors remain parallel

## Slide 3: Review: Types of Axonometric Projections
q 1
q 3
q 2
There are the three most common types of axonometric projections. They can be distinguished by counting how many angles of a projected cube are similar
None = trimetric
Two = dimetric
Three = isometric
Theta=angle
e.g. 120,120,120
Notes: These types of axonometric projections are determined by how many angles of a corner of a projected cube are the same.? In the Dimetric, two angles are the same, in Trimetric, none are the same.
There are any number of axonometric projections. Simply by changing the angle of projection, we can get any image we want.
Oh, by the way, three of those are very popular and have been given a name by the number of angles that are the same.
They are available in your view menu in SW.

## Slide 4: Review: What is an Oblique Projection?
Oblique projectors have a slanting position or direction. It’s not the orientation of the object.
- They are neither perpendicular nor horizontal, a non right-angle relationship between projectors and projection plane.
Notes: -An oblique drawing is a type of pictorial with the longest dimension or front parallel to the PP.
-The front view is shown in true shape and true size.
-The other views (e.g. sides) are parallel but can vary from 0 -90 degrees (arbitrarily).
- They can have a slanting position or direction; They are neither perpendicular nor horizontal, a non-right angle

## Slide 5: Learning objectives for week 6
Auxiliary view
Cross-section view
Degrees of Freedom
Notes: Define an auxiliary view, label fold lines, and create an auxiliary view given a multi-view drawing.
Define a cross-section, list the line conventions used in a cross-section, create a cross-section given an isometric or multi-view drawing
Describe the differences between a part and an assembly, understand the purpose of constraints, create an assembly in SolidWorks given the necessary parts

## Slide 6: Why do we need Auxiliary Views?
The true shape and size of objects having inclined or oblique surfaces can not be drawn using the regular top, front, right and left side views.

## Slide 7: Inclined & Oblique: Faces and Edges
Both faces and edges can be inclined or oblique.
Inclined face: perpendicular but not parallel to a principal plane.
Oblique face: neither perpendicular nor parallel to a principal plane
Inclined edge: parallel to a principal plane, but not perpendicular to any other principal plane.
Oblique edge: not parallel to any principal plane.

## Slide 8: Inclined & Oblique: Faces and Edges
Both faces and edges can be inclined or oblique.
Principal face: appears as a polygon in one view and edges in the other two views.
Inclined face: appears as a polygon in two views and an edge in the other view.
Oblique face: appears as a polygon in all three views.

## Slide 9: Inclined & Oblique: Faces and Edges
Both faces and edges can be inclined or oblique.
Principal edge: appears as an edge in two views and a point in the other view
Inclined edge: appears as an edge in all three views
Oblique edge: appears as an edge in all three views

## Slide 10: The Need for Auxiliary Views
http://www.soundcraft.com/product_sheet.asp?product_id=22
Notes: -This mixing board has an incline with features e.g. button and sliders that can not be shown from only one view.
-We can not ascertain the true length of the inclined face from this pictorial, nor can we get the true width from this pictorial view.

## Slide 11: The Need for Auxiliary Views
http://www.soundcraft.com/product_sheet.asp?product_id=22
An auxiliary view would give you the true shape of the inclined face of this sound mixer

## Slide 12: Why do we need Auxiliary Views?
?
?
?
What is the true shape and
size of the inclined face?

## Slide 13: Why do we need Auxiliary Views?
The correct auxiliary view is perpendicular to the face for which you seek a true shape view.

## Slide 14: What is an Auxiliary View?
Definition:
An auxiliary view is an orthographic view that is not one of the six standard projection e.g. plan (top, front, right side etc.)
Auxiliary views allows us to view faces of features that are not parallel to the standard planes of projection to appear True Shape ‘TS’ and Size.
To get TS, you need to have True Length and True Width.
True Shape and Size views can be dimensioned
Notes: Simply said: Aux. Views are views that allow hidden faces to be shown in their True Shape. If we look at that control panel straight, on, it is distorted or obscured.

## Slide 15: Creating an Auxiliary View
Notes: How are you going to show the distorted shape as a True Shape?
The inclined face is distorted at top view and right side view
So, primary views do not give all of the information in this case.

## Slide 16: A key principle for auxiliary views
A
A
Distances between points are the same in related views.
Notes: How are you going to show the distorted shape as a True Shape?
The inclined face is distorted at top view and right side view
So, primary views do not give all of the information in this case.

## Slide 17: Key principle #2 for auxiliary views
A True Shape view is perpendicular to a surface viewed on edge.
A
A
A
B
B
, B
D
D
D ,
C
C
C
F=Front
1
Line of sight
(LOS)
F
An auxiliary view is perpendicular to the view from which it is derived.
Notes: How are you going to show the distorted shape as a True Shape?
The inclined face is distorted at top view and right side view
So, primary views do not give all of the information in this case.

## Slide 18: Drawing an Auxiliary View
Precaution:
When drawing auxiliary views, the usual practice is to show only the true shape portion of the view.
It is usually not necessary to draw a full projection of the object, just the face in question.

## Slide 19: Creating an Aux View (1)
Steps
1) Label points
A
A
A
B
B
, B
D
D
D ,
C
C
C
Notes: Notice how line A, B and then C,D correspond to the face on the isometric.
-We have labeled the face in clockwise fashion.
-Notice how face 1 (red outline) which labels the auxiliary view, is parallel to A,B,C and D.
Important: When you draw the aux. view, it should always project from the view that shows the TL of the incline
In the drawing above, the front view shows TL.
-
Top View: Y is the distance back from the front plane to line that defines the beginning of the AB line (how far it is projected off- notice it is paralle to the ABCD face
X is the distance from the same plane to the back of the object.
All of the x,y distances are the same…they are adjacent to the front view
It is inherent in the glass box idea.

## Slide 20: Creating an Aux View (1)
Steps
1) Label points
A
A
A
B
B
, B
D
D
D ,
C
C
C
Notes: Notice how line A, B and then C,D correspond to the face on the isometric.
-We have labeled the face in clockwise fashion.
-Notice how face 1 (red outline) which labels the auxiliary view, is parallel to A,B,C and D.
Important: When you draw the aux. view, it should always project from the view that shows the TL of the incline
In the drawing above, the front view shows TL.
-
Top View: Y is the distance back from the front plane to line that defines the beginning of the AB line (how far it is projected off- notice it is paralle to the ABCD face
X is the distance from the same plane to the back of the object.
All of the x,y distances are the same…they are adjacent to the front view
It is inherent in the glass box idea.

## Slide 21: Creating an Aux View (2)
Steps
Label points
Create fold line
A
A
A
B
B
, B
D
D
D ,
C
C
C
F=Front
1
Line of sight
(LOS)
F
Notes: Fold line is:
-Exactly the same as the seam on the glass box. You can basically put it anywhere you want.

## Slide 22: Creating an Aux View (3 & 4)
Steps
Label points
Create fold line
Create other fold
lines
4) Put in projectors
To produce a true shape view, the face to be viewed
must appear as a line in the
source view AND the
projection must be
perpendicular to that line.
A
A
A
B
B
, B
D
D
D ,
C
C
C
F
1=Aux Plane
H=Horizontal
F
Right Side
F=Front
Notes: -The projectors or construction lines must always be at right angles to the angled surface!
-In other words, the auxiliary view is constructed perpendicularly to the incline line (front view)
-The fold lines show the edges of the top and right side (they are blue in colour)

## Slide 23: Creating an Aux View (5)
Steps
Label points
Create fold line
Create other fold
lines
4) Put in projectors
Transfer
measurements
A
A
A
B
B
, B
D
D
D ,
C
C
C
F
1
H
F
F
P=Profile
A
D
B
C
P

## Slide 24: Creating an Aux View (6)
Steps
Label points
Create fold line
Create other fold
lines
4) Put in projectors
Transfer
measurements
6) Connect points
A
A
A
B
B
, B
D
D
D ,
C
C
C
F
1
H
F
F
P
A
D
B
C

## Slide 25: Creating an Aux View (complete)
Steps
Label points
Create fold line
Create other fold
lines
4) Put in projectors
Transfer
measurements
6) Connect points
A
A
A
B
B
, B
D
D
D ,
C
C
C
F
1
H
F
F
P
A
D
B
C
Notes: Remove all of the construction lines
Notice how in the side view A and D are foreshortened compared to A and D in the auxiliary view
B and C are foreshortened in the plan view compared to the aux view.

## Slide 26: Types of Auxiliary Views
Primary Auxiliary View:
  projection from one of the six principal views
  A primary auxiliary view is projected onto a plane that is perpendicular to one of the principal planes of projection and is inclined to the other two
Notes: Use second, this plan

## Slide 27: Auxiliary Views
Notes: -Here is an odd object with faces at strange angles. It is important to see these faces face on. There are three different faces. You don’t normally worry about the angle of the face, you just take them off in the x and y directions.
Requiring three auxiliary views
-Same idea as before…the auxiliary views are projected from the inclined face
-Here are some faces that are at a strange angle, but we can really see what’s going on on those faces.

## Slide 28: Types of Auxiliary Views
Secondary Auxiliary View:
  projected from a primary auxiliary view
Tertiary Auxiliary View:
  projected from a secondary or another tertiary auxiliary view
Notes: Why do you need a secondary aux. view? (Ask John) or tertiary for that matter?

## Slide 29: Partial Auxiliary View
Don’t show other features
Easier to draw
Easier to understand
Unless otherwise specified, we will create partial auxiliary views in IAT106
Notes: -We will only add partial auxiliary views because they are easier to draw
-A full auxiliary view will show everything you see looking at that direction but there is more information than we need
- We are only looking at the face parallel to the auxiliary plane.

## Slide 30
In-class exercise: Follow along with this auxiliary exercise using pencil and grid paper: 2 minutes

## Slide 31
Tools for auxiliary views: Compass (or dividers) and straightedge allowed, indeed encouraged!

## Slide 32: Cross-sections

## Slide 33: What are Sectional Views?
When there are complicated internal features, they may be hard to identify in normal views with hidden lines.
A view with some of the part "cut away" can make the internal features very easy to see, these are called section views.

## Slide 34: The Need for Cross-sections
http://www.geodegallery.com/coconuts/wholecoconuts.html

## Slide 35: Cross-sections: Internal Combustion Engines
http://www.youtube.com/watch?v=UT6XVLSM0vA&feature=related
Forest Edwards Radial 5 Engine - Section View

## Slide 36: Tree Cross-sections
http://cache.eb.com/eb/image?id=72251&rendTypeId=35
http://www.backyardnature.net/woodtwi2.htm

## Slide 37: Biological Cross-sections
http://www.npr.org/templates/story/story.php?storyId=5640183
http://www.infovisual.info/03/036_en.html
Notes: A 3d model has been created…how can we see the complex structure within. One way to make the cut and
Remove the material on one side of the cut.

## Slide 38: Creating a Cross-section
Normal
Multi-view
Correct
Cross-section
Incorrect
Cross-section

## Slide 39: Creating a Cross-section
Normal
Multi-view
Correct
Cross-section
Incorrect
Cross-section

## Slide 40: Creating a Cross-section
Normal
Multiview
Correct
Cross-section
Incorrect
Cross-section
Notes: when there are complicated internal features, they may be hard to identify in normal views with hidden lines. A view with some of the part "cut away" can make the internal features very easy to see, these are called section views.
In these views hidden lines are generally not used, except for clarity in some cases.
The cutting plane for the section is,
- shown with thick black dashed lines.
- has arrows at the end of the line to indicate the view direction
- has letters placed beside the arrow heads. These will identify the section
- does not have to be a straight line
sections can be lined to indicate,
- when the section plane slices through material
- two methods for representing materials. First, use 45° lines, and refer to material in title block. If there are multiple materials, lines at 30° and 60° may be used for example. Second, use a conventional set of fill lines to represent the different types of materials.

## Slide 41: Advice for Creating a Cross-section
Notes: We now put a cutting plane where the cutting line is. If we just see the material that has been cut, this is what we see.
The arrows show the direction of the cross-section. The actual cross-section is on the opposite side where the arrows point.
We need to fill in the lines, because we would see what is on the other side of the cutting.

## Slide 42: Orientation of Cutting Plane
In their orientation sections are very much like multi-views!
Notes: -Why is right side better? View should be on the opposite side of the arrows.
-You are removing all of the material to the right of the material and looking at it on the direction of the arrows.

## Slide 43: Creating a cross-section

## Slide 44: Creating a cross-section (2)
Notes: We are going to draw a cross-section in lieu of a top view
The cross-section is looking down. If you look through it, you can see the various parts looking down.
The channel is still there, but we can’t see it.

## Slide 45: Creating a cross-section (3)
Notes: The hatched lines is the cross-section

## Slide 46: Offset Cutting Planes
Notes: The whole notion is that features are not all in a straight line, but you can show a slight variation using offset cutting planes to show interesting stuff. On the left, you want to show both holes, so you put a jog in the plane. On the right, you have to put a cutting plane at an angle to show the notched hole.

## Slide 47: Oversized Objects
When a small cross section and of some length has to be drawn, there are two choices:
If the drawing is made full size, it may be too large to fit on your sheet
If the drawing is reduced in scale, the details may be too small to give the required information or to be dimensioned.
In such cases, the object can be reduced in length via a Conventional Break.
Notes: What do you do if you are showing the section of a long pipe- you would need to scale down the drawing significantly or

## Slide 48: Conventional Break
"Conventional " here means
"as a matter of practice", not
"normal, unexceptional".
http://draftingmanuals.tpub.com/14276/img/14276_189_1.jpg
Notes: What do you do if you are showing the section of a long pipe- you would need to scale down the drawing significantly or

## Slide 49
In-class exercise--Follow along with this cross-section exercise:

## Slide 50: Degrees of Freedom

## Slide 51: Degrees of Freedom
Consider a single object that is a rigid body:
http://www1.istockphoto.com/file_thumbview_approve/
2272757/2/istockphoto_2272757_cooked_spaghetti.jpg
http://www.arcadeshopper.com/mame/images/hammer.jpg
Rigid Body
Non-rigid Body
Notes: For the purpose of this course, we are only going to talk about rigid bodies e.g. block or hammer- something that is absolutely rigid, but it can be rotated in space. A plate of spaghetti has noodles that are infinitely flexible.

## Slide 52: Degrees of Freedom (For a Rigid Body)
The number of variables needed to describe the position and orientation of an object in space.
Divide movement into two types:
  Translational (think of side to side, laterally)
  Rotational (think of twisting)

## Slide 53: Example of 1 Degree of Freedom
0
Consider a creature that lives on a number line in a 1 dimensional world
x
0
x
Creature can go forward and backward -> 1 degree of freedom
Notes: An example of one degree of freedom, an object can move forwards and backwards on a line. It can change only one thing…it’s position on that line.

## Slide 54: Example of 3 Degrees of Freedom
Consider a creature that lives in 2 dimensions.
x
y
If he can move along the x and y axis and can not rotate, that is 2 DOF.
Move along the x and y axis
as well as rotate -> 3DOF
Notes: You can move the creature laterally up and down.

## Slide 55: Example of 6 Degrees of Freedom
Now Consider three dimensions
x
y
z
Translate on x, y, and z
Rotate about x, y, z
Roll
Pitch
Yaw
http://www.nasm.si.edu/exhibitions/gal109/NEWHTF/ROLL.HTM
-> 6 DOF

## Slide 56: How Many Degrees of Freedom in a Merry-Go-Round?
Now Consider three dimensions
x
y
z
Notes: Horses have two degrees of freedom with respect to the merry go round– can go up and down on the pole and can rotate.

## Slide 57: DOF Summary
Translate along an axis
Rotate about an axis
1 Dimension -> 1 DOF
2 Dimension -> 3 DOF
3 Dimension -> 6 DOF
Notes: 2D – three degrees of freedom x and y (square on a page, the square could move up to the y, to the x and it could spin.) translate x or y and spin (one direction or counterclockwise)
-In a three dimensional world an object has six degrees of freedom
3D – six degrees of freedom x,y, and z. (move the cube up to the x,y or z and it can spin) You can translate and spin on each axis. With six degrees of freedom, the cube can be in anywhere in space.

## Slide 58: Mates in OnShape
Mates capability:
  Mates are another name for constraints
  regulates degree of freedom when components brought together in assembly

## Slide 59: Mate Types
Planar Mates
Planar – superimposes two selected entities – point, line, plane
  Planar (touching) A planar mate forces two planar faces to become coplanar.
  The faces can move along one another but cannot be pulled apart.
http://sahajpanchal.wordpress.com/2011/12/28/assembly-mates-in-solidworksstandard-mates/

## Slide 60: Mate Types
Parallel Mates
Parallel – makes two selected entities parallel.
Possible between lines and planes only. Requires linear/planner elements to be selected. You can use this mate to make side faces of the links parallel.
http://sahajpanchal.wordpress.com/2011/12/28/assembly-mates-in-solidworksstandard-mates/

## Slide 61: Mate Types
Perpendicular
Planar mate at 90 degrees angle
Aligns two lines and/or planes normal to each other.
Requires linear/planner elements to be selected.
http://sahajpanchal.wordpress.com/2011/12/28/assembly-mates-in-solidworksstandard-mates/

## Slide 62: Mate Types
Tangent
Tangent (plane that touches a curve or curved surface at any point)
This mate is useful when you want to define sliding contact between surfaces or curves.
In the example, cylindrical face of the follower is tangent to the top face of the valve.
http://sahajpanchal.wordpress.com/2011/12/28/assembly-mates-in-solidworksstandard-mates/
In this example by the way the pin slot mate can also be used.

## Slide 63: Mate Types
Revolute
Revolute – makes the two selected cylindrical/conical faces share the same axis.
Well, not only faces, but you can select circular edges or sketch elements as well.
In the image below, the mate makes the selected holes concentric.
http://sahajpanchal.wordpress.com/2011/12/28/assembly-mates-in-solidworksstandard-mates/

## Slide 64: Examples of Mates
Notes: In SolidWorks and physics world, a constraint removes one of more degrees of freedom two parts.
-Show the crank from SW. Stamper and crank the wheels

## Slide 65: Examples of Mates
Notes: In SolidWorks and physics world, a constraint removes one of more degrees of freedom two parts.
-Show the crank from SW. Stamper and crank the wheels

## Slide 66: This Week’s Lab
Completing exercises related to auxiliary views, and cross-sections, as well as creating assemblies on OnShape
BRING: pencil, eraser, graph paper, plain paper, and textbook.
Assigned readings:
  Auxiliary Views: Chapter 6 6.1 to 6.2.7 and 6.3.4
  Cross-sections: Chapter 8 8.1-8.2 and 8.4.1-8.4.6