## Slide 1: Tutorial Outline
Time | Topic
9:00 am – 9:30 am | Introduction
9:30 am – 10:10 am | Standalone Accelerator Simulation: Aladdin
10:10 am – 10:30 am | Standalone Accelerator Generation: High-Level Synthesis
10:30 am – 11:00 am | HLS-Based Accelerator-Rich Architecture Simulation: PARADE
11:00 am – 11:30 am | Break
11:30 am – 12:00 pm | Pre-RTL SoC Simulation: gem5-Aladdin
12:00 pm – 12:30 pm | FPGA Prototyping: ARACompiler
12:30 pm – 2:00 pm | Lunch
2:00 pm – 3:00 pm | Panel on Accelerator Research
3:00 pm – 3:30 pm | Accelerator Benchmarks and Workload Characterization
3:30 pm – 4:00 pm | Break
4:00 pm – 5:00 pm | Hands-on Exercise

## Slide 2: PARADE: A Cycle-Accurate Full-System Simulation Platform for Accelerator-Rich Architectural Design and Exploration
Zhenman Fang, Michael Gill
Jason Cong, Glenn Reinman
Center for Domain-Specific Computing
Center for Future Architectures Research
Computer Science Department, UCLA
[ICCAD 15]

## Slide 3: The Power Wall and Customized Computing
Source: Shekhar Borkar, Intel
Parallelization
Adapt the architecture to
application domain
Customization

## Slide 4: The Trend of Accelerator-Rich Architecture (ARA)
Global Accelerator Manager (GAM) with shared TLB
From ARC [DAC 12] & CHARM [DAC 14]

## Slide 5: Our Motivation and Goal
A stack of research tools for accelerator-rich architecture
  Standalone accelerator simulation: Aladdin
  Standalone accelerator generation: HLS
  System-level HLS-based ARA simulation: PARADE
  System-level pre-RTL SoC simulation: gem5 + Aladdin
  ARA FPGA prototyping: ARACompiler
Spare the community the difficulties we have encountered
Accelerate the adoption of accelerator-rich architecture (ARA)
early-stage
late-stage

## Slide 6: PARADE: Platform for Accelerator-Rich Architectural Design & Exploration [ICCAD 15]
extended m5 (McPAT) for X86 CPU, with OS
auto-generated accelerators based on HLS (AutoPilot)
added SPM, DMA, GAM & TLB model
extended Ruby (CACTI) for
coherent cache hierarchy
gem5 memory model [ISPASS 14]
extended Garnet
(DSENT) for NoC

## Slide 7: HLS-based Automatic Accelerator Generation
Program Generator
Application Dataflow
Accelerator
Source Code
Simulation Module Generator
Accelerators chaining info
Simulation
module info
Simulation Module
High-Level Synthesis
C function to accelerate
Timing info e.g., II, clk
RTL Synthesis
RTL model
Output
Tool
Input
Handles accelerator communication, task buffer, interrupts, …
Generated Program

## Slide 8: Visualization Support
router_0
core_0
L1D_0
L2_0
router_3
L1D_3
acc_1
L2_3
router_1
L1D_1
acc_0
L2_1
router_2
GAM
L1D_2
L2_2
mc_0
According to the component’s utilization, assign a different color.
The dark red indicates a potential bottleneck!

## Slide 9: Tutorial Agenda
Building the PARADE simulator
Creating a benchmark
Running a benchmark on PARADE
Performance and energy analysis using PARADE
  Performance breakdown
  Energy breakdown
Simulation speed of PARADE
Summary of PARADE features

## Slide 10: Building PARADE
Use an existing accelerator module: VectorAddSample
  #include "VectorAddSample.hh” in LCAccOperatingModeInclude.hh
    VectorAddSample.hh contains accelerator modeling details
  REGISTER_OPMODE(OperatingMode_VectorAddSample) in LCAccOperatingModeListing.hh
  g_LCAccInterface->AddOperatingMode(g_LCAccDeviceHandle[0], "VectorAddSample"); in startup() mem/ruby/system/System.cc
The same compiling command as gem5 (32nm @2GHz)
  scons PROTOCOL=MESI_Two_Level_Trace build/X86/gem5.opt

## Slide 11: Adding an Accelerator Simulation Module
User high-level description: VectorAddSample.type
1390 uw
52806 um2
10
2 (1GHz)
1
Replace timing by our HLS/RTL tool
./run.autopilot.sh VectorAddSample.type
Specify an unique accelerator module name and opcode
Specify accelerator
inputs and outputs
Specify accelerator computation body: one iteration in the loop

## Slide 12: Auto-Generated Accelerator Simulation Module
Auto-generated accelerator module: VectorAddSample.hh
each accelerator inherits the LCAccOperationMode class
accelerator module name and opcode
accelerator timing
info from HLS/RTL
auto-generated SPM address mapping
model SPM/DMA timing, and computation latency
mono AccGen.exe -path:src/modules/LCAcc VectorAddSample.type

## Slide 13: Creating a Benchmark
To use existing accelerators, just call accelerator API
base BenchmarkNode class
Create a BenchmarkNode, call Initialize() and Run()
inherit BenchmarkNode
include accelerator API
call the CreateBuffer API to init the accelerator, write the program description to memory buffer
call the run_buf API to read the accelerator, run it, handle the communication with CPU and GAM

## Slide 14: Within the Accelerator Library (for Benchmarks)
New ISA
lcacc-req type
lcacc-rsrv id, time
lcacc-cmd id, cmd, addr
lcacc-free id
Mem
Task description
Request available accelerators (lcacc-req)
Response available ones & waiting time
Request reservation (lcacc-rsv) and wait
Reserve accelerator, send it the core ID
The core shares a task description and start the accelerator (lcacc-cmd)
4
CPU
GAM
Acc
1
2
3
4
4
5
5
6
7
Read task & start work
Work done, notify the core
Free accelerators (lcacc-free)
Users don’t have to worry about these, we provide a dataflow language and tool to automatically generate the library

## Slide 15: Creating an Accelerator Library (for Benchmarks)
To create an accelerator library, specify accelerator dataflow
input and output
whole data size and tile size
task based on tile size (chunk)
use double SPM buffer
declare the accelerator
create SPM for input/output
data transfer based on tile:
input LLC/DRAM -> SPM &
output SPM -> LLC/DRAM
trigger accelerator within tile:
input SPM -> Register & output Register -> SPM
(mono ApGen.exe VectorAddSample.txt VectorAddSampleLCacc.h)

## Slide 16: Running a Benchmark on PARADE
Similar gem5 command to run benchmarks
  ./gem5.opt --outdir=./TDLCA_BlackScholes/ configs/example/fs.py full-system config
  --checkpoint-dir=./ckpt-1core/ --restore-with-cpu=timing -r 1 -n 1 restore checkpoint
  -s 16565183 -W 16565183 timing warmup initialization, then switch to OoO
  --ruby --l2_size=64kB --num-l2caches=32 32-banked 2MB LLC with Ruby
  --mem-size=2GB --num-dirs=4 2GB memory with 4 DDR3 controllers
  --garnet=fixed --topology=Mesh --mesh-rows=4 4*8 mesh with Garnet
  --lcacc --accelerators=1 1 copy of accelerator
  --script=./configs/boot/BlackScholes.td.rcS BlackScholes boot script
  >& TDLCA_BlackScholes/result.txt redirect output to result.txt
Output statistics of PARADE
  Stats.txt, result.txt, and visual.txt (visualization trace)

## Slide 17: Execution Cycles for BlackScholes
Chart: Execution cycles
| Total | Computation | Non-overlapped Communication
BlackScholes-SW | 297386293 | 162608827 | 134777466
BlackScholes-dedicated-ARA | 3150663 | 1048576 | 2102087
94X
155X
64X

## Slide 18: Execution Cycles for BlackScholes (cont.)
Total cycles: check stats.txt
  system.switch_cpus_1.numCycles 3158763
CPU/SW computation time (assume perfect cache)
  Change configuration to use 20MB L2 cache with 1 cycle latency
ARA computation/communication time
  Result.txt contains start, and end time for each task computation and data transfer
  Postprocessing “ResultParser result.txt”, it will generate

## Slide 19: Issuing IPC Breakdown for BlackScholes
Chart: # of issued instructions per cycle on CPU (BlackScholes)
| issue_0 | issue_1 | issue_2 | issue_3 | issue_4 | issue_5 | issue_6 | issue_7 | issue_8
 | 0.6168 | 0.1475 | 0.0684 | 0.0515 | 0.048 | 0.0304 | 0.013 | 0.0129 | 0.0116
No issuing instruction
For the accelerator version, it’s customized to a fully-utilized 234-stage deep pipeline

## Slide 20: Issuing IPC Breakdown for BlackScholes (cont.)
Check stats.txt
ARA version based on HLS
  ./run.autopilot.sh BlackScholes.type

## Slide 21: # of Cache/Memory Access for BlackScholes
Chart: # of accesses
| L1D/SPM | L1I | LLC | Memory
BlackScholes-SW | 77937166 | 42376518 | 770192 | 450544
BlackScholes-dedicated-ARA | 1835008 | 0 | 533145 | 450298
42X L1D reduction by removing register spilling
removed instructions
no notable reduction

## Slide 22: # of Cache/Memory Access for BlackScholes (cont.)
Check stats.txt

## Slide 23: Cache/Memory Bandwidth for BlackScholes
Chart: Bandwidth (MB/s)
| L1D/SPM | LLC | Memory
BlackScholes-SW | 33545.4508 | 331.5034 | 193.9216
BlackScholes-dedicated-ARA | 74549.7135 | 21659.7459 | 18293.973
improved LLC/DRAM effective bandwidth
Bandwidth = Access * 64B * 10-6/ (Cycles/2GHz) (MB/s)

## Slide 24: Energy Breakdown for Deblur
Chart: Energy breakdown for dedicated ARA (Deblur)
| Core_Acc | LLC | NoC | DRAM
 | 0.19653 | 0.16047 | 0.096669 | 0.92841

## Slide 25: Energy Breakdown for Deblur (cont.)
Energy = power * time, we measure power directly
Accelerator power: given by run.autopilot.sh
DRAM power (gem5 integrated Micron model, ISPASS 14)
  system.mem_ctrls0.averagePower::0 753.996167 in stats.txt
Core power (McPAT)
  generate.mcpat.xml.sh convert gem5 statistics to mcpat xml
  generate.mcpat.energy.sh generate power numbers

## Slide 26: Energy Breakdown for Deblur (cont.)
LLC power (CACTI, integrated with McPAT)
NoC power (DSENT)
  run generate.dsent.sh

## Slide 27: Simulation Speed of PARADE
Chart: gem5 KIPS
| Deblur | Denoise | Registration | Segmentation | BlackScholes | StreamCluster | Swaptions | LPCIP_Desc | Texture_Synthesis | Robot_Localization | Disparity_Map | EKF_SLAM | Medical Imaging | Commercial | Vision | Navigation
gem5-SW_KIPS | 31.9447 | 33.7932 | 22.0211 | 23.0496 | 33.2729 | 30.4465 | 52.7075 | 47.0486 | 47.6797 | 25.4001 | 13.9423 | 28.7738
PARADE-dedicated-ARA-speedup | 1.4604 | 1.3301 | 1.4854 | 6.4312 | 4.6058 | 0.76461 | 15.4257 | 1.9635 | 2.6821 | 1.7236 | 4.4328 | 1.0171
15X
KIPS: Kilo Instructions simulated Per Second

## Slide 28: PARADE: Platform for ARA Design & Exploration
Based on widely-used gem5 and support full-system X86
Global Accelerator Management (GAM)
Coherent cache/SPM with shared memory (Ruby)
Customizable Network-on-Chip simulation (Garnet)
Power/area simulation
  McPAT for CPUs; high-level synthesis (AutoPilot) for accelerators
  CACTI for caches; DSENT for NoC, Micron model for DRAM
Visualization to assist design space exploration

## Slide 29: Thank You!
For more information, please contact Zhenman Fang, zhenman@cs.ucla.edu
Tutorial website: http://accelerator.eecs.harvard.edu/isca15tutorial/