Solutions Manual

for

Introduction to Thermodynamics and Heat Transfer

Yunus A. Cengel

2nd Edition, 2008

Chapter 6

MASS AND ENERGY ANALYSIS OF CONTROL VOLUMES

# PROPRIETARY AND CONFIDENTIAL

This Manual is the proprietary property of The McGraw-Hill Companies, Inc. (“McGraw-Hill”) and protected by copyright and other state and federal laws.  By opening and using this Manual the user agrees to the following restrictions, and if the recipient does not agree to these restrictions, the Manual should be promptly returned unopened to McGraw-Hill:  This Manual is being provided only to authorized professors and instructors for use in preparing for the classes using the affiliated textbook.  No other use or distribution of this Manual is permitted.  This Manual may not be sold and may not be distributed to or used by any student or other third party.  No part of this Manual may be reproduced, displayed or distributed in any form or by any means, electronic or otherwise, without the prior written permission of McGraw-Hill.

Conservation of Mass

6-1C Mass, energy, momentum, and electric charge are conserved, and volume and entropy are not conserved during a process.

6-2C Mass flow rate is the amount of mass flowing through a cross-section per unit time whereas the volume flow rate is the amount of volume flowing through a cross-section per unit time.

6-3C The amount of mass or energy entering a control volume does not have to be equal to the amount of mass or energy leaving during an unsteady-flow process.

6-4C Flow through a control volume is steady when it involves no changes with time at any specified position.

6-5C No, a flow with the same volume flow rate at the inlet and the exit is not necessarily steady (unless the density is constant). To be steady, the mass flow rate through the device must remain constant.

6-6E A garden hose is used to fill a water bucket. The volume and mass flow rates of water, the filling time, and the discharge velocity are to be determined.

Assumptions 1 Water is an incompressible substance. 2 Flow through the hose is steady. 3 There is no waste of water by splashing.

Properties We take the density of water to be 62.4 lbm/ft3 (Table A-3E).

Analysis (a) The volume and mass flow rates of water are

(b) The time it takes to fill a 20-gallon bucket is

(c) The average discharge velocity of water at the nozzle exit is

Discussion Note that for a given flow rate, the average velocity is inversely proportional to the square of the velocity. Therefore, when the diameter is reduced by half, the velocity quadruples.

6-7 Air is accelerated in a nozzle. The mass flow rate and the exit area of the nozzle are to be determined.

Assumptions Flow through the nozzle is steady.

Properties The density of air is given to be 2.21 kg/m3 at the inlet, and 0.762 kg/m3 at the exit.

Analysis (a) The mass flow rate of air is determined from the inlet conditions to be

(b) There is only one inlet and one exit, and thus . Then the exit area of the nozzle is determined to be

6-8E Steam flows in a pipe. The minimum diameter of the pipe for a given steam velocity is to be determined.

Assumptions Flow through the pipe is steady.

Properties The specific volume of steam at the given state is (Table A-6E)

Analysis The cross sectional area of the pipe is

Solving for the pipe diameter gives

# Therefore, the diameter of the pipe must be at least 3.63 ft to ensure that the velocity does not exceed 59 ft/s.

6-9  A water pump increases water pressure. The diameters of the inlet and exit openings are given. The velocity of the water at the inlet and outlet are to be determined.

Assumptions 1 Flow through the pump is steady. 2 The specific volume remains constant.

Properties The inlet state of water is compressed liquid. We approximate it as a saturated liquid at the given temperature. Then, at 15°C and 40°C, we have (Table A-4)

Analysis The velocity of the water at the inlet is

Since the mass flow rate and the specific volume remains constant, the velocity at the pump exit is

Using the specific volume at 40°C, the water velocity at the inlet becomes

which is a 0.8% increase in velocity.

6-10 Air is expanded and is accelerated as it is heated by a hair dryer of constant diameter. The percent increase in the velocity of air as it flows through the drier is to be determined.

Assumptions Flow through the nozzle is steady.

Properties The density of air is given to be 1.20 kg/m3 at the inlet, and 1.05 kg/m3 at the exit.

Analysis There is only one inlet and one exit, and thus . Then,

Therefore, the air velocity increases 14% as it flows through the hair drier.

6-11 A rigid tank initially contains air at atmospheric conditions. The tank is connected to a supply line, and air is allowed to enter the tank until the density rises to a specified level. The mass of air that entered the tank is to be determined.

Properties The density of air is given to be 1.18 kg/m3 at the beginning, and 7.20 kg/m3 at the end.

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary.  The mass balance for this system can be expressed as

Mass balance:

Substituting,

Therefore, 6.02 kg of mass entered the tank.

# 6-12 A smoking lounge that can accommodate 15 smokers is considered. The required minimum flow rate of air that needs to be supplied to the lounge and the diameter of the duct are to be determined.

Assumptions  Infiltration of air into the smoking lounge is negligible.

Properties The minimum fresh air requirements for a smoking lounge is given to be 30 L/s per person.

Analysis The required minimum flow rate of air that needs to be supplied to the lounge is determined directly from

The volume flow rate of fresh air can be expressed as

Solving for the diameter D and substituting,

Therefore, the diameter of the fresh air duct should be at least 26.8 cm if the velocity of air is not to exceed 8 m/s.

6-13 The minimum fresh air requirements of a residential building is specified to be 0.35 air changes per hour. The size of the fan that needs to be installed and the diameter of the duct are to be determined.

Analysis   The volume of the building and the required minimum volume flow rate of fresh air are

The volume flow rate of fresh air can be expressed as

Solving for the diameter D and substituting,

Therefore, the diameter of the fresh air duct should be at least 10.6 cm if the velocity of air is not to exceed 6 m/s.

6-14 A cyclone separator is used to remove fine solid particles that are suspended in a gas stream. The mass flow rates at the two outlets and the amount of fly ash collected per year are to be determined.

Assumptions  Flow through the separator is steady.

Analysis Since the ash particles cannot be converted into the gas and vice-versa, the mass flow rate of ash into the control volume must equal that going out, and the mass flow rate of flue gas into the control volume must equal that going out. Hence, the mass flow rate of ash leaving is

The mass flow rate of flue gas leaving the separator is then

The amount of fly ash collected per year is

6-15 Air flows through an aircraft engine. The volume flow rate at the inlet and the mass flow rate at the exit are to be determined.

Assumptions 1 Air is an ideal gas. 2 The flow is steady.

Properties The gas constant of air is R = 0.287 kPa(m3/kg(K (Table A-1).

Analysis  The inlet volume flow rate is

The specific volume at the inlet is

Since the flow is steady, the mass flow rate remains constant during the flow. Then,

6-16 A spherical hot-air balloon is considered. The time it takes to inflate the balloon is to be determined.

Assumptions 1 Air is an ideal gas.

Properties The gas constant of air is R = 0.287 kPa(m3/kg(K (Table A-1).

Analysis  The specific volume of air entering the balloon is

The mass flow rate at this entrance is

The initial mass of the air in the balloon is

Similarly, the final mass of air in the balloon is

The time it takes to inflate the balloon is determined from

6-17 Water flows through the tubes of a boiler. The velocity and volume flow rate of the water at the inlet are to be determined.

Assumptions Flow through the boiler is steady.

Properties The specific volumes of water at the inlet and exit are (Tables A-6 and A-7)

Analysis The cross-sectional area of the tube is

The mass flow rate through the tube is same at the inlet and exit. It may be determined from exit data to be

The water velocity at the inlet is then

The volumetric flow rate at the inlet is

6-18 Refrigerant-134a flows through a pipe. Heat is supplied to R-134a. The volume flow rates of air at the inlet and exit, the mass flow rate, and the velocity at the exit are to be determined.

Properties The specific volumes of R-134a at the inlet and exit are (Table A-13)

Analysis (a) (b) The volume flow rate at the inlet and the mass flow rate are

(c) Noting that mass flow rate is constant, the volume flow rate and the velocity at the exit of the pipe are determined from

# Flow Work and Energy Transfer by Mass

6-19C  Energy can be transferred to or from a control volume as heat, various forms of work, and by mass.

6-20C  Flow energy or flow work is the energy needed to push a fluid into or out of a control volume. Fluids at rest do not possess any flow energy.

6-21C  Flowing fluids possess flow energy in addition to the forms of energy a fluid at rest possesses. The total energy of a fluid at rest consists of internal, kinetic, and potential energies. The total energy of a flowing fluid consists of internal, kinetic, potential, and flow energies.

6-22E Steam is leaving a pressure cooker at a specified pressure. The velocity, flow rate, the total and flow energies, and the rate of energy transfer by mass are to be determined.

Assumptions 1 The flow is steady, and the initial start-up period is disregarded. 2 The kinetic and potential energies are negligible, and thus they are not considered. 3 Saturation conditions exist within the cooker at all times so that steam leaves the cooker as a saturated vapor at 30 psia.

Properties The properties of saturated liquid water and water vapor at 30 psia are vf = 0.01700 ft3/lbm, vg = 13.749 ft3/lbm, ug = 1087.8 Btu/lbm, and hg = 1164.1 Btu/lbm (Table A-5E).

Analysis (a) Saturation conditions exist in a pressure cooker at all times after the steady operating conditions are established. Therefore, the liquid has the properties of saturated liquid and the exiting steam has the properties of saturated vapor at the operating pressure. The amount of liquid that has evaporated, the mass flow rate of the exiting steam, and the exit velocity are

(b) Noting that h = u + Pv and that the kinetic and potential energies are disregarded, the flow and total energies of the exiting steam are

Note that the kinetic energy in this case is ke = V2/2 = (15.4 ft/s)2 = 237 ft2/s2 = 0.0095 Btu/lbm, which is very small compared to enthalpy.

(c) The rate at which energy is leaving the cooker by mass is simply the product of the mass flow rate and the total energy of the exiting steam per unit mass,

Discussion The numerical value of the energy leaving the cooker with steam alone does not mean much since this value depends on the reference point selected for enthalpy (it could even be negative). The significant quantity is the difference between the enthalpies of the exiting vapor and the liquid inside  (which is hfg) since it relates directly to the amount of energy supplied to the cooker.

6-23 Air flows steadily in a pipe at a specified state. The diameter of the pipe, the rate of flow energy, and the rate of energy transport by mass are to be determined. Also, the error involved in the determination of energy transport by mass is to be determined.

Properties The properties of air are R = 0.287 kJ/kg.K and cp = 1.008 kJ/kg.K (at 350 K from Table A-2b)

Analysis (a) The diameter is determined as follows

(b) The rate of flow energy is determined from

(c) The rate of energy transport by mass is

(d) If we neglect kinetic energy in the calculation of energy transport by mass

Therefore, the error involved if neglect the kinetic energy is only 0.09%.

6-24E A water pump increases water pressure. The flow work required by the pump is to be determined.

Assumptions 1 Flow through the pump is steady. 2 The state of water at the pump inlet is saturated liquid. 3 The specific volume remains constant.

Properties The specific volume of saturated liquid water at 10 psia is

(Table A-5E)

Then the flow work relation gives

6-25 An air compressor compresses air. The flow work required by the compressor is to be determined.

Assumptions 1 Flow through the compressor is steady. 2 Air is an ideal gas.

Properties Combining the flow work expression with the ideal gas equation of state gives

# Steady Flow Energy Balance: Nozzles and Diffusers

6-26C  A steady-flow system involves no changes with time anywhere within the system or at the system boundaries

6-27C  No.

6-28C  It is mostly converted to internal energy as shown by a rise in the fluid temperature.

6-29C  The kinetic energy of a fluid increases at the expense of the internal energy as evidenced by a decrease in the fluid temperature.

6-30C  Heat transfer to the fluid as it flows through a nozzle is desirable since it will probably increase the kinetic energy of the fluid. Heat transfer from the fluid will decrease the exit velocity.

6-31 Air is accelerated in a nozzle from 30 m/s to 180 m/s. The mass flow rate, the exit temperature, and the exit area of the nozzle are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Air is an ideal gas with constant specific heats. 3 Potential energy changes are negligible. 4 The device is adiabatic and thus heat transfer is negligible. 5 There are no work interactions.

Properties The gas constant of air is 0.287 kPa.m3/kg.K (Table A-1). The specific heat of air at the anticipated average temperature of 450 K is cp = 1.02 kJ/kg.(C (Table A-2).

Analysis (a) There is only one inlet and one exit, and thus . Using the ideal gas relation, the specific volume and the mass flow rate of air are determined to be

(b) We take nozzle as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Substituting,

It yields		T2 = 184.6(C

(c)  The specific volume of air at the nozzle exit is

→ A2 = 0.00387 m2 = 38.7 cm2

6-32 EES Problem 6-31 is reconsidered. The effect of the inlet area on the mass flow rate, exit velocity, and the exit area as the inlet area varies from 50 cm2 to 150 cm2 is to be investigated, and the final results are to be plotted against the inlet area.

Analysis The problem is solved using EES, and the solution is given below.

Function HCal(WorkFluid$, Tx, Px)

"Function to calculate the enthalpy of an ideal gas or real gas"

If   'Air' = WorkFluid$  then

HCal:=ENTHALPY('Air',T=Tx) "Ideal gas equ."

else

HCal:=ENTHALPY(WorkFluid$,T=Tx, P=Px)"Real gas equ."

endif

end  HCal

"System: control volume for the nozzle"

"Property relation: Air is an ideal gas"

"Process: Steady state, steady flow, adiabatic, no work"

"Knowns - obtain from the input diagram"

WorkFluid$ = 'Air'

T[1] = 200  [C]

P[1] = 300   [kPa]

Vel[1] = 30  [m/s]

P[2] = 100  [kPa]

Vel[2] = 180  [m/s]

A[1]=80 [cm^2]

Am[1]=A[1]*convert(cm^2,m^2)

"Property Data - since the Enthalpy function has different parameters

for ideal gas and real fluids, a function was used to determine h."

h[1]=HCal(WorkFluid$,T[1],P[1])

h[2]=HCal(WorkFluid$,T[2],P[2])

"The Volume function has the same form for an ideal gas as for a real fluid."

v[1]=volume(workFluid$,T=T[1],p=P[1])

v[2]=volume(WorkFluid$,T=T[2],p=P[2])

"Conservation of mass: "

m_dot[1]= m_dot[2]

"Mass flow rate"

m_dot[1]=Am[1]*Vel[1]/v[1]

m_dot[2]= Am[2]*Vel[2]/v[2]

"Conservation of Energy - SSSF energy balance"

h[1]+Vel[1]^2/(2*1000) = h[2]+Vel[2]^2/(2*1000)

"Definition"

A_ratio=A[1]/A[2]

A[2]=Am[2]*convert(m^2,cm^2)

| A1 [cm2] | A2 [cm2] | m1 | T2 |
| --- | --- | --- | --- |
| 50 | 24.19 | 0.3314 | 184.6 |
| 60 | 29.02 | 0.3976 | 184.6 |
| 70 | 33.86 | 0.4639 | 184.6 |
| 80 | 38.7 | 0.5302 | 184.6 |
| 90 | 43.53 | 0.5964 | 184.6 |
| 100 | 48.37 | 0.6627 | 184.6 |
| 110 | 53.21 | 0.729 | 184.6 |
| 120 | 58.04 | 0.7952 | 184.6 |
| 130 | 62.88 | 0.8615 | 184.6 |
| 140 | 67.72 | 0.9278 | 184.6 |
| 150 | 72.56 | 0.9941 | 184.6 |

6-33E Air is accelerated in an adiabatic nozzle. The velocity at the exit is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Air is an ideal gas with constant specific heats. 3 Potential energy changes are negligible. 4 There are no work interactions. 5 The nozzle is adiabatic.

Properties The specific heat of air at the average temperature of (700+645)/2=672.5°F is cp = 0.253 Btu/lbm(R (Table A-2Eb).

Analysis There is only one inlet and one exit, and thus . We take nozzle as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Solving for exit velocity,

6-34 Air is decelerated in an adiabatic diffuser. The velocity at the exit is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Air is an ideal gas with constant specific heats. 3 Potential energy changes are negligible. 4 There are no work interactions. 5 The diffuser is adiabatic.

Properties The specific heat of air at the average temperature of (20+90)/2=55°C =328 K is cp = 1.007 kJ/kg(K (Table A-2b).

Analysis There is only one inlet and one exit, and thus . We take diffuser as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Solving for exit velocity,

6-35 Steam is accelerated in a nozzle from a velocity of 80 m/s. The mass flow rate, the exit velocity, and the exit area of the nozzle are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Potential energy changes are negligible. 3 There are no work interactions.

Properties From the steam tables (Table A-6)

and

Analysis (a)  There is only one inlet and one exit, and thus . The mass flow rate of steam is

(b) We take nozzle as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Substituting, the exit velocity of the steam is determined to be

It yields				V2 = 562.7 m/s

(c) The exit area of the nozzle is determined from

6-36 CD EES Steam is accelerated in a nozzle from a velocity of 40 m/s to 300 m/s. The exit temperature and the ratio of the inlet-to-exit area of the nozzle are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Potential energy changes are negligible. 3 There are no work interactions. 4 The device is adiabatic and thus heat transfer is negligible.

Properties From the steam tables (Table A-6),

Analysis  (a) There is only one inlet and one exit, and thus . We take nozzle as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

or,

Thus,

(b)  The ratio of the inlet to exit area is determined from the conservation of mass relation,

6-37 Air is decelerated in a diffuser from 230 m/s to 30 m/s. The exit temperature of air and the exit area of the diffuser are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Air is an ideal gas with variable specific heats. 3 Potential energy changes are negligible. 4 The device is adiabatic and thus heat transfer is negligible. 5 There are no work interactions.

Properties The gas constant of air is 0.287 kPa.m3/kg.K (Table A-1). The enthalpy of air at the inlet temperature of 400 K is h1 = 400.98 kJ/kg (Table A-21).

Analysis  (a) There is only one inlet and one exit, and thus . We take diffuser as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

,

or,

From Table A-21,	T2 = 425.6 K

(b)  The specific volume of air at the diffuser exit is

From conservation of mass,

6-38E Air is decelerated in a diffuser from 600 ft/s to a low velocity. The exit temperature and the exit velocity of air are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Air is an ideal gas with variable specific heats. 3 Potential energy changes are negligible. 4 The device is adiabatic and thus heat transfer is negligible. 5 There are no work interactions.

Properties The enthalpy of air at the inlet temperature of 20(F is h1 = 114.69 Btu/lbm (Table A-21E).

Analysis  (a) There is only one inlet and one exit, and thus . We take diffuser as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

,

or,

From Table A-21E,		T2 = 510.0 R

(b)  The exit velocity of air is determined from the conservation of mass relation,

Thus,

6-39 CO2 gas is accelerated in a nozzle to 450 m/s. The inlet velocity and the exit temperature are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 CO2 is an ideal gas with variable specific heats. 3 Potential energy changes are negligible. 4 The device is adiabatic and thus heat transfer is negligible. 5 There are no work interactions.

Properties The gas constant and molar mass of CO2 are 0.1889 kPa.m3/kg.K and 44 kg/kmol (Table A-1). The enthalpy of CO2 at 500(C is 30,797 kJ/kmol (from CO2 ideal gas tables -not available in this text).

Analysis (a) There is only one inlet and one exit, and thus . Using the ideal gas relation, the specific volume is determined to be

Thus,

(b)  We take nozzle as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Substituting,

Then the exit temperature of CO2 from the ideal gas tables is obtained to be      T2 = 685.8 K

Alternative Solution Using constant specific heats for CO2 at an anticipated average temperature of 700 K (Table A-2b), from the energy balance we obtain

The result is practically identical to the result obtained earlier.

6-40 R-134a is accelerated in a nozzle from a velocity of 20 m/s. The exit velocity of the refrigerant and the ratio of the inlet-to-exit area of the nozzle are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Potential energy changes are negligible. 3 There are no work interactions. 4 The device is adiabatic and thus heat transfer is negligible.

Properties From the refrigerant tables (Table A-13)

and

Analysis (a) There is only one inlet and one exit, and thus . We take nozzle as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Substituting,

It yields		 V2 = 409.9 m/s

(b)  The ratio of the inlet to exit area is determined from the conservation of mass relation,

6-41 Nitrogen is decelerated in a diffuser from 200 m/s to a lower velocity. The exit velocity of nitrogen and the ratio of the inlet-to-exit area are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Nitrogen is an ideal gas with variable specific heats. 3 Potential energy changes are negligible. 4 The device is adiabatic and thus heat transfer is negligible. 5 There are no work interactions.

Properties The molar mass of nitrogen is M = 28 kg/kmol (Table A-1). The enthalpies are (from nitrogen ideal gas tables-not available in this text)

Analysis  (a) There is only one inlet and one exit, and thus . We take diffuser as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

,

Substituting,

It yields				       V2 = 93.0 m/s

(b)  The ratio of the inlet to exit area is determined from the conservation of mass relation,

or,

Alternative Solution Using constant specific heats for N2 at room temperature (Table A-2a), from the energy balance we obtain

The result is practically identical to the result obtained earlier.

6-42 EES Problem 6-41 is reconsidered. The effect of the inlet velocity on the exit velocity and the ratio of the inlet-to-exit area as the inlet velocity varies from 180 m/s to 260 m/s is to be investigated. The final results are to be plotted against the inlet velocity.

Analysis The problem is solved using EES, and the solution is given below.

Function HCal(WorkFluid$, Tx, Px)

"Function to calculate the enthalpy of an ideal gas or real gas"

If   'N2' = WorkFluid$  then

HCal:=ENTHALPY(WorkFluid$,T=Tx) "Ideal gas equ."

else

HCal:=ENTHALPY(WorkFluid$,T=Tx, P=Px)"Real gas equ."

endif

end  HCal

"System: control volume for the nozzle"

"Property relation: Nitrogen is an ideal gas"

"Process: Steady state, steady flow, adiabatic, no work"

"Knowns"

WorkFluid$ = 'N2'

T[1] = 7  [C]

P[1] = 60   [kPa]

{Vel[1] = 200  [m/s]}

P[2] = 85  [kPa]

T[2] = 22 [C]

"Property Data - since the Enthalpy function has different parameters

for ideal gas and real fluids, a function was used to determine h."

h[1]=HCal(WorkFluid$,T[1],P[1])

h[2]=HCal(WorkFluid$,T[2],P[2])

"The Volume function has the same form for an ideal gas as for a real fluid."

v[1]=volume(workFluid$,T=T[1],p=P[1])

v[2]=volume(WorkFluid$,T=T[2],p=P[2])

"From the definition of mass flow rate, m_dot = A*Vel/v and conservation of mass the area ratio A_Ratio = A_1/A_2 is:"

A_Ratio*Vel[1]/v[1] =Vel[2]/v[2]

"Conservation of Energy - SSSF energy balance"

h[1]+Vel[1]^2/(2*1000) = h[2]+Vel[2]^2/(2*1000)

| ARatio | Vel1 [m/s] | Vel2 [m/s] |
| --- | --- | --- |
| 0.2603 | 180 | 34.84 |
| 0.4961 | 190 | 70.1 |
| 0.6312 | 200 | 93.88 |
| 0.7276 | 210 | 113.6 |
| 0.8019 | 220 | 131.2 |
| 0.8615 | 230 | 147.4 |
| 0.9106 | 240 | 162.5 |
| 0.9518 | 250 | 177 |
| 0.9869 | 260 | 190.8 |

6-43 R-134a is decelerated in a diffuser from a velocity of 120 m/s. The exit velocity of R-134a and the mass flow rate of the R-134a are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Potential energy changes are negligible. 3 There are no work interactions.

Properties From the R-134a tables (Tables A-11 through A-13)

and

Analysis (a)  There is only one inlet and one exit, and thus . Then the exit velocity of R-134a is determined from the steady-flow mass balance to be

(b) We take diffuser as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Substituting, the mass flow rate of the refrigerant is determined to be

It yields

6-44 Heat is lost from the steam flowing in a nozzle. The velocity and the volume flow rate at the nozzle exit are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Potential energy change is negligible. 3 There are no work interactions.

Analysis We take the steam as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Energy balance:

or

The properties of steam at the inlet and exit are (Table A-6)

The mass flow rate of the steam is

Substituting,

The volume flow rate at the exit of the nozzle is

# Turbines and Compressors

6-45C  Yes.

6-46C  The volume flow rate at the compressor inlet will be greater than that at the compressor exit.

6-47C  Yes. Because energy (in the form of shaft work) is being added to the air.

6-48C  No.

6-49 Air is expanded in a turbine. The mass flow rate and outlet area are to be determined.

Assumptions 1 Air is an ideal gas. 2 The flow is steady.

Properties The gas constant of air is R = 0.287 kPa(m3/kg(K (Table A-1).

Analysis  The specific volumes of air at the inlet and outlet are

The mass flow rate is

The outlet area is

6-50E Air is expanded in a gas turbine. The inlet and outlet mass flow rates are to be determined.

Assumptions 1 Air is an ideal gas. 2 The flow is steady.

Properties The gas constant of air is R = 0.3704 psia(ft3/lbm(R (Table A-1E).

Analysis  The specific volumes of air at the inlet and outlet are

The volume flow rates at the inlet and exit are then

6-51 Air is compressed at a rate of 10 L/s by a compressor. The work required per unit mass and the power required are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible.  3 Air is an ideal gas with constant specific heats.

Properties The constant pressure specific heat of air at the average temperature of (20+300)/2=160°C=433 K is cp = 1.018 kJ/kg·K (Table A-2b). The gas constant of air is R = 0.287 kPa(m3/kg(K (Table A-1).

Analysis (a) There is only one inlet and one exit, and thus . We take the compressor as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Thus,

(b) The specific volume of air at the inlet and the mass flow rate are

Then the power input is determined from the energy balance equation to be

6-52 Steam expands in a turbine. The change in kinetic energy, the power output, and the turbine inlet area are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Potential energy changes are negligible. 3 The device is adiabatic and thus heat transfer is negligible.

Properties From the steam tables (Tables A-4 through 6)

and

Analysis (a) The change in kinetic energy is determined from

(b) There is only one inlet and one exit, and thus . We take the turbine as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Then the power output of the turbine is determined by substitution to be

(c)  The inlet area of the turbine is determined from the mass flow rate relation,

6-53 EES Problem 6-52 is reconsidered. The effect of the turbine exit pressure on the power output of the turbine as the exit pressure varies from 10 kPa to 200 kPa is to be investigated. The power output is to be plotted against the exit pressure.

Analysis The problem is solved using EES, and the solution is given below.

"Knowns "

T[1] = 450 [C]

P[1] = 10000  [kPa]

Vel[1] = 80  [m/s]

P[2] = 10  [kPa]

X_2=0.92

Vel[2] = 50  [m/s]

m_dot[1]=12 [kg/s]

Fluid$='Steam_IAPWS'

"Property Data"

h[1]=enthalpy(Fluid$,T=T[1],P=P[1])

h[2]=enthalpy(Fluid$,P=P[2],x=x_2)

T[2]=temperature(Fluid$,P=P[2],x=x_2)

v[1]=volume(Fluid$,T=T[1],p=P[1])

v[2]=volume(Fluid$,P=P[2],x=x_2)

"Conservation of mass: "

m_dot[1]= m_dot[2]

"Mass flow rate"

m_dot[1]=A[1]*Vel[1]/v[1]

m_dot[2]= A[2]*Vel[2]/v[2]

"Conservation of Energy - Steady Flow energy balance"

m_dot[1]*(h[1]+Vel[1]^2/2*Convert(m^2/s^2, kJ/kg)) = m_dot[2]*(h[2]+Vel[2]^2/2*Convert(m^2/s^2, kJ/kg))+W_dot_turb*convert(MW,kJ/s)

DELTAke=Vel[2]^2/2*Convert(m^2/s^2, kJ/kg)-Vel[1]^2/2*Convert(m^2/s^2, kJ/kg)

| P2 [kPa] | Wturb [MW] | T2 [C] |
| --- | --- | --- |
| 10 | 10.22 | 45.81 |
| 31.11 | 9.66 | 69.93 |
| 52.22 | 9.377 | 82.4 |
| 73.33 | 9.183 | 91.16 |
| 94.44 | 9.033 | 98.02 |
| 115.6 | 8.912 | 103.7 |
| 136.7 | 8.809 | 108.6 |
| 157.8 | 8.719 | 112.9 |
| 178.9 | 8.641 | 116.7 |
| 200 | 8.57 | 120.2 |

6-54 Steam expands in a turbine. The mass flow rate of steam for a power output of 5 MW is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 The device is adiabatic and thus heat transfer is negligible.

Properties From the steam tables (Tables A-4 through 6)

Analysis There is only one inlet and one exit, and thus . We take the turbine as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Substituting, the required mass flow rate of the steam is determined to be

6-55E Steam expands in a turbine. The rate of heat loss from the steam for a power output of 4 MW is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible.

Properties From the steam tables (Tables A-4E through 6E)

Analysis There is only one inlet and one exit, and thus . We take the turbine as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Substituting,

6-56 Steam expands in a turbine. The exit temperature of the steam for a power output of 2 MW is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 The device is adiabatic and thus heat transfer is negligible.

Properties From the steam tables (Tables A-4 through 6)

Analysis  There is only one inlet and one exit, and thus . We take the turbine as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Substituting,

Then the exit temperature becomes

6-57 Argon gas expands in a turbine. The exit temperature of the argon for a power output of 250 kW is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Potential energy changes are negligible. 3 The device is adiabatic and thus heat transfer is negligible. 4 Argon is an ideal gas with constant specific heats.

Properties The gas constant of Ar is R = 0.2081 kPa.m3/kg.K. The constant pressure specific heat of Ar is cp = 0.5203 kJ/kg·(C (Table A-2a)

Analysis There is only one inlet and one exit, and thus . The inlet specific volume of argon and its mass flow rate are

Thus,

We take the turbine as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Substituting,

It yields

T2 = 267.3(C

6-58 Helium is compressed by a compressor. For a mass flow rate of 90 kg/min, the power input required is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible.  3 Helium is an ideal gas with constant specific heats.

Properties The constant pressure specific heat of helium is cp = 5.1926 kJ/kg·K (Table A-2a).

Analysis There is only one inlet and one exit, and thus . We take the compressor as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Thus,

6-59 CO2 is compressed by a compressor. The volume flow rate of CO2 at the compressor inlet and the power input to the compressor are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible.  3 Helium is an ideal gas with variable specific heats. 4 The device is adiabatic and thus heat transfer is negligible.

Properties The gas constant of CO2 is R = 0.1889 kPa.m3/kg.K, and its molar mass is M = 44 kg/kmol (Table A-1). The inlet and exit enthalpies of CO2 are (from CO2 ideal gas tables –not available in this text)

Analysis (a) There is only one inlet and one exit, and thus . The inlet specific volume of air and its volume flow rate are

(b) We take the compressor as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Substituting

Alternative Solution Using constant specific heats for CO2 at room temperature (Table A-2a), from the energy balance we obtain

The result is close to the result obtained earlier.

6-60 Air is expanded in an adiabatic turbine. The mass flow rate of the air and the power produced are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 The turbine is well-insulated, and thus there is no heat transfer.  3 Air is an ideal gas with constant specific heats.

Properties The constant pressure specific heat of air at the average temperature of (500+150)/2=325°C=598 K is cp = 1.051 kJ/kg·K (Table A-2b). The gas constant of air is R = 0.287 kPa(m3/kg(K (Table A-1).

Analysis (a) There is only one inlet and one exit, and thus . We take the turbine as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

The specific volume of air at the inlet and the mass flow rate are

Similarly at the outlet,

(b) Substituting into the energy balance equation gives

6-61 Air is compressed in an adiabatic compressor. The mass flow rate of the air and the power input are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 The compressor is adiabatic.  3 Air is an ideal gas with constant specific heats.

Properties The constant pressure specific heat of air at the average temperature of (20+400)/2=210°C=483 K is cp = 1.026 kJ/kg·K (Table A-2b). The gas constant of air is R = 0.287 kPa(m3/kg(K (Table A-1).

Analysis (a) There is only one inlet and one exit, and thus . We take the compressor as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

The specific volume of air at the inlet and the mass flow rate are

Similarly at the outlet,

(b) Substituting into the energy balance equation gives

6-62E Air is expanded in an adiabatic turbine. The mass flow rate of the air and the power produced are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 The turbine is well-insulated, and thus there is no heat transfer.  3 Air is an ideal gas with constant specific heats.

Properties The constant pressure specific heat of air at the average temperature of (800+250)/2=525°F is cp = 0.2485 Btu/lbm·R (Table A-2Eb). The gas constant of air is R = 0.3704 psia(ft3/lbm(R (Table A-1E).

Analysis There is only one inlet and one exit, and thus . We take the turbine as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

The specific volume of air at the exit and the mass flow rate are

Similarly at the inlet,

Substituting into the energy balance equation gives

6-63 Steam expands in a two-stage adiabatic turbine from a specified state to another state. Some steam is extracted at the end of the first stage. The power output of the turbine is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 The turbine is adiabatic and thus heat transfer is negligible.

Properties From the steam tables (Table A-6)

Analysis The mass flow rate through the second stage is

We take the entire turbine, including the connection part between the two stages, as the system, which is a control volume since mass crosses the boundary. Noting that one fluid stream enters the turbine and two fluid streams leave, the energy balance for this steady-flow system can be expressed in the rate form as

Substituting, the power output of the turbine is

# Throttling Valves

6-64C  Yes.

6-65C  No. Because air is an ideal gas and h = h(T) for ideal gases.  Thus if h remains constant, so does the temperature.

6-66C  If it remains in the liquid phase, no. But if some of the liquid vaporizes during throttling, then yes.

6-67C The temperature of a fluid can increase, decrease, or remain the same during a throttling process. Therefore, this claim is valid since no thermodynamic laws are violated.

6-68 Refrigerant-134a is throttled by a capillary tube. The quality of the refrigerant at the exit is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 Heat transfer to or from the fluid is negligible. 4 There are no work interactions involved.

Analysis There is only one inlet and one exit, and thus . We take the throttling valve as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

since .

The inlet enthalpy of R-134a is, from the refrigerant tables (Table A-11),

The exit quality is

6-69 Steam is throttled from a specified pressure to a specified state. The quality at the inlet is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 Heat transfer to or from the fluid is negligible. 4 There are no work interactions involved.

Analysis There is only one inlet and one exit, and thus . We take the throttling valve as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

since .

The enthalpy of steam at the exit is (Table A-6),

The quality of the steam at the inlet is (Table A-5)

6-70 CD EES Refrigerant-134a is throttled by a valve. The pressure and internal energy after expansion are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 Heat transfer to or from the fluid is negligible. 4 There are no work interactions involved.

Properties The inlet enthalpy of R-134a is, from the refrigerant tables (Tables A-11 through 13),

Analysis There is only one inlet and one exit, and thus . We take the throttling valve as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

since . Then,

Obviously hf < h2 <hg, thus the refrigerant exists as a saturated mixture at the exit state, and thus

P2  =  Psat @ -20°C  =  132.82 kPa

Also,

Thus,

6-71 Steam is throttled by a well-insulated valve. The temperature drop of the steam after the expansion is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 Heat transfer to or from the fluid is negligible. 4 There are no work interactions involved.

Properties The inlet enthalpy of steam is (Tables A-6),

Analysis There is only one inlet and one exit, and thus . We take the throttling valve as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

since . Then the exit temperature of steam becomes

6-72 EES Problem 6-71 is reconsidered. The effect of the exit pressure of steam on the exit temperature after throttling as the exit pressure varies from 6 MPa to 1 MPa is to be investigated.  The exit temperature of steam is to be plotted against the exit pressure.

Analysis The problem is solved using EES, and the solution is given below.

"Input information from Diagram Window"

{WorkingFluid$='Steam_iapws' "WorkingFluid: can be  changed to ammonia or other fluids"

P_in=8000 [kPa]

T_in=500  [C]

P_out=6000  [kPa]}

$Warning off

"Analysis"

m_dot_in=m_dot_out  "steady-state mass balance"

m_dot_in=1  "mass flow rate is arbitrary"

m_dot_in*h_in+Q_dot-W_dot-m_dot_out*h_out=0  "steady-state energy balance"

Q_dot=0  "assume the throttle to operate adiabatically"

W_dot=0  "throttles do not have any means of producing power"

h_in=enthalpy(WorkingFluid$,T=T_in,P=P_in)  "property table lookup"

T_out=temperature(WorkingFluid$,P=P_out,h=h_out)  "property table lookup"

x_out=quality(WorkingFluid$,P=P_out,h=h_out)  "x_out is the quality at the outlet"

P[1]=P_in;  P[2]=P_out;  h[1]=h_in;  h[2]=h_out  "use arrays to place points on property plot"

| Pout [kPa] | Tout [C] |
| --- | --- |
| 1000 | 463.1 |
| 2000 | 468.8 |
| 3000 | 474.3 |
| 4000 | 479.7 |
| 5000 | 484.9 |
| 6000 | 490.1 |

6-73E  High-pressure air is throttled to atmospheric pressure. The temperature of air after the expansion is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 Heat transfer to or from the fluid is negligible. 4 There are no work interactions involved. 5 Air is an ideal gas.

Analysis There is only one inlet and one exit, and thus . We take the throttling valve as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

since .

For an ideal gas,

h = h(T).

Therefore,

T2 = T1 = 90°F

6-74 Carbon dioxide flows through a throttling valve. The temperature change of CO2 is to be determined if CO2 is assumed an ideal gas and a real gas.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 Heat transfer to or from the fluid is negligible. 4 There are no work interactions involved.

Analysis There is only one inlet and one exit, and thus . We take the throttling valve as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

since .

(a) For an ideal gas,  h = h(T), and therefore,

(b) We obtain real gas properties of CO2 from EES software as follows

Note that EES uses a different reference state from the textbook for CO2 properties. The temperature difference in this case becomes

That is, the temperature of CO2 decreases by 34(C in a throttling process if its real gas properties are used.

# Mixing Chambers and Heat Exchangers

6-75C  Yes, if the mixing chamber is losing heat to the surrounding medium.

6-76C Under the conditions of no heat and work interactions between the mixing chamber and the surrounding medium.

6-77C Under the conditions of no heat and work interactions between the heat exchanger and the surrounding medium.

6-78 A hot water stream is mixed with a cold water stream. For a specified mixture temperature, the mass flow rate of cold water is to be determined.

Assumptions 1 Steady operating conditions exist. 2 The mixing chamber is well-insulated so that heat loss to the surroundings is negligible. 3 Changes in the kinetic and potential energies of fluid streams are negligible. 4 Fluid properties are constant. 5 There are no work interactions.

Properties Noting that T < Tsat @ 250 kPa = 127.41°C, the water in all three streams exists as a compressed liquid, which can be approximated as a saturated liquid at the given temperature.  Thus,

h1  (  hf @ 80(C  =	335.02 kJ/kg

h2  (  hf @ 20(C  =	  83.915 kJ/kg

h3  (  hf @ 42(C  =	175.90 kJ/kg

Analysis We take the mixing chamber as the system, which is a control volume. The mass and energy balances for this steady-flow system can be expressed in the rate form as

Mass balance:

Energy balance:

Combining the two relations and solving for  gives

Substituting, the mass flow rate of cold water stream is determined to be

6-79E Liquid water is heated in a chamber by mixing it with saturated water vapor. If both streams enter at the same rate, the temperature and quality (if saturated) of the exit stream is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions. 4 The device is adiabatic and thus heat transfer is negligible.

Properties From steam tables (Tables A-5E through A-6E),

h1  (  hf @ 50(F   =   18.07 Btu/lbm

h2  =  hg @ 50 psia = 1174.2 Btu/lbm

Analysis   We take the mixing chamber as the system, which is a control volume since mass crosses the boundary. The mass and energy balances for this steady-flow system can be expressed in the rate form as

Mass balance:

Energy balance:

Combining the two gives

Substituting,

h3  =  (18.07 + 1174.2)/2 = 596.16 Btu/lbm

At 50 psia, hf = 250.21 Btu/lbm and hg = 1174.2 Btu/lbm.  Thus the exit stream is a saturated mixture since hf < h3 < hg.  Therefore,

T3 = Tsat @ 50 psia = 280.99(F

and

0.374

6-80 Two streams of refrigerant-134a are mixed in a chamber. If the cold stream enters at twice the rate of the hot stream, the temperature and quality (if saturated) of the exit stream are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions. 4 The device is adiabatic and thus heat transfer is negligible.

Properties From R-134a tables (Tables A-11 through A-13),

h1  (  hf @ 12(C   =  68.18 kJ/kg

h2  =  h @ 1 MPa,  60(C = 293.38 kJ/kg

Analysis   We take the mixing chamber as the system, which is a control volume since mass crosses the boundary. The mass and energy balances for this steady-flow system can be expressed in the rate form as

Mass balance:

Energy balance:

Combining the two gives

Substituting,

h3 = (2(68.18 + 293.38)/3 = 143.25 kJ/kg

At 1 MPa, hf = 107.32 kJ/kg and hg = 270.99 kJ/kg.  Thus the exit stream is a saturated mixture since

hf < h3 < hg.  Therefore,

T3 = Tsat @ 1 MPa = 39.37(C

and

0.220

6-81 EES Problem 6-80 is reconsidered. The effect of the mass flow rate of the cold stream of R-134a on the temperature and the quality of the exit stream as the ratio of the mass flow rate of the cold stream to that of the hot stream varies from 1 to 4 is to be investigated. The mixture temperature and quality are to be plotted against the cold-to-hot mass flow rate ratio.

Analysis The problem is solved using EES, and the solution is given below.

"Input Data"

"m_frac = 2"  "m_frac =m_dot_cold/m_dot_hot= m_dot_1/m_dot_2"

T[1]=12 [C]

P[1]=1000 [kPa]

T[2]=60 [C]

P[2]=1000 [kPa]

m_dot_1=m_frac*m_dot_2

P[3]=1000 [kPa]

m_dot_1=1

"Conservation of mass for the R134a: Sum of m_dot_in=m_dot_out"

m_dot_1+ m_dot_2 =m_dot_3

"Conservation of Energy for steady-flow: neglect changes in KE and PE"

"We assume no heat transfer and no work occur across the control surface."

E_dot_in - E_dot_out = DELTAE_dot_cv

DELTAE_dot_cv=0   "Steady-flow requirement"

E_dot_in=m_dot_1*h[1] + m_dot_2*h[2]

E_dot_out=m_dot_3*h[3]

"Property data are given by:"

h[1] =enthalpy(R134a,T=T[1],P=P[1])

h[2] =enthalpy(R134a,T=T[2],P=P[2])

T[3] =temperature(R134a,P=P[3],h=h[3])

x_3=QUALITY(R134a,h=h[3],P=P[3])

| mfrac | T3 [C] | x3 |
| --- | --- | --- |
| 1 | 39.37 | 0.4491 |
| 1.333 | 39.37 | 0.3509 |
| 1.667 | 39.37 | 0.2772 |
| 2 | 39.37 | 0.2199 |
| 2.333 | 39.37 | 0.174 |
| 2.667 | 39.37 | 0.1365 |
| 3 | 39.37 | 0.1053 |
| 3.333 | 39.37 | 0.07881 |
| 3.667 | 39.37 | 0.05613 |
| 4 | 39.37 | 0.03649 |

6-82 Refrigerant-134a is condensed in a water-cooled condenser. The mass flow rate of the cooling water  required is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions. 4 Heat loss from the device to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid.

Properties  The enthalpies of R-134a at the inlet and the exit states are (Tables A-11 through A-13)

Water exists as compressed liquid at both states, and thus (Table A-4)

h1  (  hf @ 15(C   =   62.98 kJ/kg

h2  (  hf @ 25(C   = 104.83 kJ/kg

Analysis We take the heat exchanger as the system, which is a control volume. The mass and energy balances for this steady-flow system can be expressed in the rate form as

Mass balance (for each fluid stream):

Energy balance (for the heat exchanger):

Combining the two,

Solving for :

Substituting,

6-83E CD EES Air is heated in a steam heating system. For specified flow rates, the volume flow rate of air at the inlet is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions. 4 Heat loss from the device to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid. 5 Air is an ideal gas with constant specific heats at room temperature.

Properties The gas constant of air is 0.3704 psia.ft3/lbm.R (Table A-1E). The constant pressure specific heat of air is cp = 0.240 Btu/lbm·°F (Table A-2E). The enthalpies of steam at the inlet and the exit states are (Tables A-4E through A-6E)

Analysis  We take the entire heat exchanger as the system, which is a control volume. The mass and energy balances for this steady-flow system can be expressed in the rate form as

Mass balance ( for each fluid stream):

Energy balance (for the entire heat exchanger):

Combining the two,

Solving for :

Substituting,

Also,

Then the volume flow rate of air at the inlet becomes

6-84 Steam is condensed by cooling water in the condenser of a power plant. If the temperature rise of the cooling water is not to exceed 10(C, the minimum mass flow rate of the cooling water required is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions. 4 Heat loss from the device to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid. 5 Liquid water is an incompressible substance with constant specific heats at room temperature.

Properties The cooling water exists as compressed liquid at both states, and its specific heat at room temperature is c = 4.18 kJ/kg·°C (Table A-3). The enthalpies of the steam at the inlet and the exit states are (Tables A-5 and A-6)

Analysis We take the heat exchanger as the system, which is a control volume. The mass and energy balances for this steady-flow system can be expressed in the rate form as

Mass balance (for each fluid stream):

Energy balance (for the heat exchanger):

Combining the two,

Solving for :

Substituting,

6-85 Ethylene glycol is cooled by water in a heat exchanger. The rate of heat transfer in the heat exchanger and the mass flow rate of water are to be determined.

Assumptions 1 Steady operating conditions exist. 2 The heat exchanger is well-insulated so that heat loss to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid. 3 Changes in the kinetic and potential energies of fluid streams are negligible. 4 Fluid properties are constant.

Properties The specific heats of water and ethylene glycol are given to be 4.18 and 2.56 kJ/kg.(C, respectively.

Analysis (a) We take the ethylene glycol tubes as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat transfer becomes

(b) The rate of heat transfer from glycol must be equal to the rate of heat transfer to the water. Then,

6-86 EES Problem 6-85 is reconsidered. The effect of the inlet temperature of cooling water on the mass flow rate of water as the inlet temperature varies from 10°C to 40°C at constant exit temperature) is to be investigated. The mass flow rate of water is to be plotted against the inlet temperature.

Analysis The problem is solved using EES, and the solution is given below.

"Input Data"

{T_w[1]=20 [C]}

T_w[2]=55 [C]  "w: water"

m_dot_eg=2 [kg/s] "eg: ethylene glycol"

T_eg[1]=80 [C]

T_eg[2]=40 [C]

C_p_w=4.18 [kJ/kg-K]

C_p_eg=2.56 [kJ/kg-K]

"Conservation of mass for the water: m_dot_w_in=m_dot_w_out=m_dot_w"

"Conservation of mass for the ethylene glycol: m_dot_eg_in=m_dot_eg_out=m_dot_eg"

"Conservation of Energy for steady-flow: neglect changes in KE and PE in each mass steam"

"We assume no heat transfer and no work occur across the control surface."

E_dot_in - E_dot_out = DELTAE_dot_cv

DELTAE_dot_cv=0 "Steady-flow requirement"

E_dot_in=m_dot_w*h_w[1] + m_dot_eg*h_eg[1]

E_dot_out=m_dot_w*h_w[2] + m_dot_eg*h_eg[2]

Q_exchanged =m_dot_eg*h_eg[1] - m_dot_eg*h_eg[2]

"Property data are given by:"

h_w[1] =C_p_w*T_w[1]  "liquid approximation applied for water and ethylene glycol"

h_w[2] =C_p_w*T_w[2]

h_eg[1] =C_p_eg*T_eg[1]

h_eg[2] =C_p_eg*T_eg[2]

| mw [kg/s] | Tw,1 [C] |
| --- | --- |
| 1.089 | 10 |
| 1.225 | 15 |
| 1.4 | 20 |
| 1.633 | 25 |
| 1.96 | 30 |
| 2.45 | 35 |
| 3.266 | 40 |

6-87 Oil is to be cooled by water in a thin-walled heat exchanger. The rate of heat transfer in the heat exchanger and the exit temperature of water is to be determined.

Assumptions 1 Steady operating conditions exist. 2 The heat exchanger is well-insulated so that heat loss to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid. 3 Changes in the kinetic and potential energies of fluid streams are negligible.  4 Fluid properties are constant.

Properties The specific heats of water and oil are given to be 4.18 and 2.20 kJ/kg.(C, respectively.

Analysis We take the oil tubes as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat transfer from the oil becomes

Noting that the heat lost by the oil is gained by the water, the outlet temperature of the water is determined from

6-88 Cold water is heated by hot water in a heat exchanger. The rate of heat transfer and the exit temperature of hot water are to be determined.

Assumptions 1 Steady operating conditions exist. 2 The heat exchanger is well-insulated so that heat loss to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid. 3 Changes in the kinetic and potential energies of fluid streams are negligible.  4 Fluid properties are constant.

Properties The specific heats of cold and hot water are given to be 4.18 and 4.19 kJ/kg.(C, respectively.

Analysis We take the cold water tubes as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat transfer to the cold water in this heat exchanger becomes

Noting that heat gain by the cold water is equal to the heat loss by the hot water, the outlet temperature of the hot water is determined to be

6-89 Air is preheated by hot exhaust gases in a cross-flow heat exchanger. The rate of heat transfer and the outlet temperature of the air are to be determined.

Assumptions 1 Steady operating conditions exist. 2 The heat exchanger is well-insulated so that heat loss to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid. 3 Changes in the kinetic and potential energies of fluid streams are negligible.  4 Fluid properties are constant.

Properties The specific heats of air and combustion gases are given to be 1.005 and 1.10 kJ/kg.(C, respectively.

Analysis We take the exhaust pipes as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat transfer from the exhaust gases becomes

The mass flow rate of air is

Noting that heat loss by the exhaust gases is equal to the heat gain by the air, the outlet temperature of the air becomes

6-90 An adiabatic open feedwater heater mixes steam with feedwater. The outlet mass flow rate and the outlet velocity are to be determined.

Assumptions Steady operating conditions exist.

Properties From a mass balance

The specific volume at the exit is (Table A-4)

The exit velocity is then

6-91E An adiabatic open feedwater heater mixes steam with feedwater. The outlet mass flow rate and the outlet velocity are to be determined for two exit temperatures.

Assumptions Steady operating conditions exist.

Properties From a mass balance

The specific volume at the exit is (Table A-4E)

The exit velocity is then

When the temperature at the exit is 180(F, we have

The mass flow rate at the exit is same while the exit velocity slightly increases when the exit temperature is 180(F instead of 120(F.

6-92 Water is heated by hot oil in a heat exchanger. The rate of heat transfer in the heat exchanger and the outlet temperature of oil are to be determined.

Assumptions 1 Steady operating conditions exist. 2 The heat exchanger is well-insulated so that heat loss to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid. 3 Changes in the kinetic and potential energies of fluid streams are negligible.  4 Fluid properties are constant.

Properties The specific heats of  water and oil are given to be 4.18 and 2.3 kJ/kg.(C, respectively.

Analysis We take the cold water tubes as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat transfer to the cold water in this heat exchanger becomes

Noting that heat gain by the water is equal to the heat loss by the oil, the outlet temperature of oil is determined from

6-93E Steam is condensed by cooling water in a condenser. The rate of heat transfer in the heat exchanger and the rate of condensation of steam are to be determined.

Assumptions 1 Steady operating conditions exist. 2 The heat exchanger is well-insulated so that heat loss to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid. 3 Changes in the kinetic and potential energies of fluid streams are negligible. 4 Fluid properties are constant.

Properties The specific heat of water is 1.0 Btu/lbm.(F (Table A-3E). The enthalpy of vaporization of water at 85(F is 1045.2 Btu/lbm (Table A-4E).

Analysis We take the tube-side of the heat exchanger where cold water is flowing as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat transfer to the cold water in this heat exchanger becomes

Noting that heat gain by the water is equal to the heat loss by the condensing steam, the rate of condensation of the steam in the heat exchanger is determined from

6-94 Two streams of cold and warm air are mixed in a chamber. If the ratio of hot to cold air is 1.6, the mixture temperature and the rate of heat gain of the room are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions. 4 The device is adiabatic and thus heat transfer is negligible.

Properties The gas constant of air is      R = 0.287 kPa.m3/kg.K. The enthalpies of air are obtained from air table (Table A-21) as

h1  = h @278 K  = 278.13 kJ/kg

h2  =  h @ 307 K = 307.23 kJ/kg

hroom  =  h @ 297 K = 297.18 kJ/kg

Analysis (a) We take the mixing chamber as the system, which is a control volume since mass crosses the boundary. The mass and energy balances for this steady-flow system can be expressed in the rate form as

Mass balance:

Energy balance:

Combining the two gives

Substituting,

h3 = (278.13 +1.6( 307.23)/2.6 = 296.04 kJ/kg

From air table at this enthalpy, the mixture temperature is

T3  = T @ h = 296.04 kJ/kg  = 295.9 K = 22.9(C

(b) The mass flow rates are determined as follows

The rate of heat gain of the room is determined from

6-95 A heat exchanger that is not insulated is used to produce steam from the heat given up by the exhaust gases of an internal combustion engine. The temperature of exhaust gases at the heat exchanger exit and the rate of heat transfer to the water are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions. 4 Exhaust gases are assumed to have air properties with constant specific heats.

Properties The constant pressure specific heat of the exhaust gases is taken to be cp = 1.045 kJ/kg·°C (Table A-2). The inlet and exit enthalpies of water are (Tables A-4 and A-5)

Analysis We take the entire heat exchanger as the system, which is a control volume. The mass and energy balances for this steady-flow system can be expressed in the rate form as

Mass balance (for each fluid stream):

Energy balance (for the entire heat exchanger):

or

Noting that the mass flow rate of exhaust gases is 15 times that of the water, substituting gives

(1)

The heat given up by the exhaust gases and heat picked up by the water are

(2)

(3)

The heat loss is

(4)

The solution may be obtained by a trial-error approach. Or, solving the above equations simultaneously using EES software, we obtain

6-96 Two streams of water are mixed in an insulated chamber. The temperature of the exit stream is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions. 4 The device is adiabatic and thus heat transfer is negligible.

Properties From the steam tables (Table A-4),

h1  (  hf @ 90(C = 377.04 kJ/kg

h2 (  hf @ 50(C = 209.34 kJ/kg

Analysis  We take the mixing chamber as the system, which is a control volume since mass crosses the boundary. The mass and energy balances for this steady-flow system can be expressed in the rate form as

Mass balance:

Energy balance:

Solving for the exit enthalpy,

The temperature corresponding to this enthalpy is

T3 =55.2(C	(Table A-4)

6-97 A chilled-water heat-exchange unit is designed to cool air by water. The maximum water outlet temperature is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions. 4 Heat loss from the device to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid. 5 Air is an ideal gas with constant specific heats at room temperature.

Properties The gas constant of air is 0.287 kPa.m3/kg.K (Table A-1). The constant pressure specific heat of air at room temperature is cp = 1.005 kJ/kg·°C (Table A-2a). The specific heat of water is 4.18 kJ/kg(K (Table A-3).

Analysis The water temperature at the heat exchanger exit will be maximum when all the heat released by the air is picked up by the water. First, the inlet specific volume and the mass flow rate of air are

We take the entire heat exchanger as the system, which is a control volume. The mass and energy balances for this steady-flow system can be expressed in the rate form as

Mass balance ( for each fluid stream):

Energy balance (for the entire heat exchanger):

Combining the two,

Solving for the exit temperature of water,

# Pipe and duct Flow

6-98 Saturated liquid water is heated in a steam boiler at a specified rate. The rate of heat transfer in the boiler is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions.

Analysis We take the pipe in which the water is heated as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

The enthalpies of water at the inlet and exit of the boiler are (Table A-5, A-6).

Substituting,

6-99 Air at a specified rate is heated by an electrical heater. The current is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 The heat losses from the air is negligible.

Properties The gas constant of air is 0.287 kPa.m3/kg.K (Table A-1). The constant pressure specific heat of air at room temperature is cp = 1.005 kJ/kg·°C (Table A-2a).

Analysis We take the pipe in which the air is heated as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

The inlet specific volume and the mass flow rate of air are

Substituting into the energy balance equation and solving for the current gives

6-100E The cooling fan of a computer draws air, which is heated in the computer by absorbing the heat of PC circuits. The electrical power dissipated by the circuits is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 All the heat dissipated by the circuits are picked up by the air drawn by the fan.

Properties The gas constant of air is 0.3704 psia·ft3/lbm·R (Table A-1E). The constant pressure specific heat of air at room temperature is cp = 0.240 Btu/lbm·°F (Table A-2Ea).

Analysis We take the pipe in which the air is heated as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

The inlet specific volume and the mass flow rate of air are

Substituting,

6-101 A desktop computer is to be cooled safely by a fan in hot environments and high elevations. The air flow rate of the fan and the diameter of the casing are to be determined.

Assumptions 1 Steady operation under worst conditions is considered. 2 Air is an ideal gas with constant specific heats. 3 Kinetic and potential energy changes are negligible.

Properties The specific heat of air at the average temperature of Tavg =  (45+60)/2 = 52.5(C = 325.5 K is cp = 1.0065 kJ/kg.(C. The gas constant for air is R = 0.287 kJ/kg.K (Table A-2).

Analysis The fan selected must be able to meet the cooling requirements of the computer at worst conditions. Therefore, we assume air to enter the computer at 66.63 kPa and 45(C, and leave at 60(C.

We take the air space in the computer as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then the required mass flow rate of air to absorb heat at a rate of 60 W is determined to be

The density of air entering the fan at the exit and its volume flow rate are

For an average exit velocity of 110 m/min, the diameter of the casing of the fan is determined from

6-102 A desktop computer is to be cooled safely by a fan in hot environments and high elevations. The air flow rate of the fan and the diameter of the casing are to be determined.

Assumptions 1 Steady operation under worst conditions is considered. 2 Air is an ideal gas with constant specific heats. 3 Kinetic and potential energy changes are negligible.

Properties The specific heat of air at the average temperature of Tave =  (45+60)/2 = 52.5(C is cp = 1.0065 kJ/kg.(C The gas constant for air is R = 0.287 kJ/kg.K (Table A-2).

Analysis The fan selected must be able to meet the cooling requirements of the computer at worst conditions. Therefore, we assume air to enter the computer at 66.63 kPa and 45(C, and leave at 60(C.

We take the air space in the computer as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then the required mass flow rate of air to absorb heat at a rate of 100 W is determined to be

The density of air entering the fan at the exit and its volume flow rate are

For an average exit velocity of 110 m/min, the diameter of the casing of the fan is determined from

6-103E Electronic devices mounted on a cold plate are cooled by water. The amount of heat generated by the electronic devices is to be determined.

Assumptions 1 Steady operating conditions exist. 2 About 15 percent of the heat generated is dissipated from the components to the surroundings by convection and radiation. 3 Kinetic and potential energy changes are negligible.

Properties The properties of water at room temperature are ( = 62.1 lbm/ft3 and cp = 1.00 Btu/lbm.(F (Table A-3E).

Analysis We take the tubes of the cold plate to be the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then mass flow rate of water and the rate of heat removal by the water are determined to be

which is 85 percent of the heat generated by the electronic devices. Then the total amount of heat generated by the electronic devices becomes

6-104 CD EES The components of an electronic device located in a horizontal duct of rectangular cross section are cooled by forced air. The heat transfer from the outer surfaces of the duct is to be determined.

Assumptions 1 Steady operating conditions exist. 2 Air is an ideal gas with constant specific heats at room temperature. 3 Kinetic and potential energy changes are negligible

Properties The gas constant of air is R  = 0.287 kJ/kg.(C (Table A-1). The specific heat of air at room temperature is cp = 1.005 kJ/kg.(C (Table A-2).

Analysis  The density of air entering the duct and the mass flow rate are

We take the channel, excluding the electronic components, to be the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat transfer to the air passing through the duct becomes

The rest of the 180 W heat generated must be dissipated through the outer surfaces of the duct by natural convection and radiation,

6-105 The components of an electronic device located in a horizontal duct of circular cross section is cooled by forced air. The heat transfer from the outer surfaces of the duct is to be determined.

Assumptions 1 Steady operating conditions exist. 2 Air is an ideal gas with constant specific heats at room temperature. 3 Kinetic and potential energy changes are negligible

Properties The gas constant of air is R  = 0.287 kJ/kg.(C (Table A-1). The specific heat of air at room temperature is cp = 1.005 kJ/kg.(C (Table A-2).

Analysis  The density of air entering the duct and the mass flow rate are

We take the channel, excluding the electronic components, to be the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat transfer to the air passing through the duct becomes

The rest of the 180 W heat generated must be dissipated through the outer surfaces of the duct by natural convection and radiation,

6-106E Water is heated in a parabolic solar collector. The required length of parabolic collector is to be determined.

Assumptions 1 Steady operating conditions exist. 2 Heat loss from the tube is negligible so that the entire solar energy incident on the tube is transferred to the water. 3 Kinetic and potential energy changes are negligible

Properties The specific heat of water at room temperature is cp = 1.00 Btu/lbm.(F (Table A-2E).

Analysis We take the thin aluminum tube to be the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then the total rate of heat transfer to the water flowing through the tube becomes

The length of the tube required is

6-107 Air enters a hollow-core printed circuit board. The exit temperature of the air is to be determined.

Assumptions 1 Steady operating conditions exist. 2 Air is an ideal gas with constant specific heats at room temperature. 3 The local atmospheric pressure is 1 atm. 4 Kinetic and potential energy changes are negligible.

Properties The gas constant of air is R  = 0.287 kJ/kg.(C (Table A-1). The specific heat of air at room temperature is cp = 1.005 kJ/kg.(C (Table A-2).

Analysis The density of air entering the duct and the mass flow rate are

We take the hollow core to be the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then the exit temperature of air leaving the hollow core becomes

6-108 A computer is cooled by a fan blowing air through the case of the computer. The required flow rate of the air and the fraction of the temperature rise of air that is due to heat generated by the fan are to be determined.

Assumptions 1 Steady flow conditions exist. 2 Air is an ideal gas with constant specific heats. 3 The pressure of air is 1 atm. 4 Kinetic and potential energy changes are negligible

Properties   The specific heat of air at room temperature is cp = 1.005 kJ/kg.(C (Table A-2).

Analysis   (a) We take the air space in the computer as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Noting that the fan power is 25 W and the 8 PCBs transfer a total of 80 W of heat to air, the mass flow rate of air is determined to be

(b) The fraction of temperature rise of air that is due to the heat generated by the fan and its motor can be determined from

6-109 Hot water enters a pipe whose outer surface is exposed to cold air in a basement. The rate of heat loss from the water is to be determined.

Assumptions 1 Steady flow conditions exist. 2 Water is an incompressible substance with constant specific heats. 3 The changes in kinetic and potential energies are negligible.

Properties  The properties of water at the average temperature of (90+88)/2 = 89(C are  and cp = 4.21 kJ/kg.(C (Table A-3).

Analysis  The mass flow rate of water is

We take the section of the pipe in the basement to be the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat transfer from the hot water to the surrounding air becomes

6-110 EES Problem 6-109 is reconsidered. The effect of the inner pipe diameter on the rate of heat loss as the pipe diameter varies from 1.5 cm to 7.5 cm is to be investigated. The rate of heat loss is to be plotted against the diameter.

Analysis The problem is solved using EES, and the solution is given below.

"Knowns:"

{D = 0.04 [m]}

rho = 965 [kg/m^3]

Vel = 0.8 [m/s]

T_1 = 90 [C]

T_2 = 88 [C]

C_P = 4.21[kJ/kg-C]

"Analysis:"

"The mass flow rate of water is:"

Area = pi*D^2/4

m_dot = rho*Area*Vel

"We take the section of the pipe in the basement to be the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as"

E_dot_in - E_dot_out = DELTAE_dot_sys

DELTAE_dot_sys = 0 "Steady-flow assumption"

E_dot_in = m_dot*h_in

E_dot_out =Q_dot_out+m_dot*h_out

h_in = C_P * T_1

h_out = C_P * T_2

| D [m] | Qout [kW] |
| --- | --- |
| 0.015 | 1.149 |
| 0.025 | 3.191 |
| 0.035 | 6.254 |
| 0.045 | 10.34 |
| 0.055 | 15.44 |
| 0.065 | 21.57 |
| 0.075 | 28.72 |

6-111 A room is to be heated by an electric resistance heater placed in a duct in the room. The power rating of the electric heater and the temperature rise of air as it passes through the heater are to be determined.

Assumptions 1 Steady operating conditions exist. 2 Air is an ideal gas with constant specific heats at room temperature. 3 Kinetic and potential energy changes are negligible. 4 The heating duct is adiabatic, and thus heat transfer through it is negligible. 5 No air leaks in and out of the room.

Properties The gas constant of air is 0.287 kPa.m3/kg.K (Table A-1). The specific heats of air at room temperature are cp = 1.005 and cv = 0.718 kJ/kg·K  (Table A-2).

Analysis (a) The total mass of air in the room is

We first take the entire room as our system, which is a closed system since no mass leaks in or out. The power rating of the electric heater is determined by applying the conservation of energy relation to this constant volume closed system:

Solving for the electrical work input gives

(b) We now take the heating duct as the system, which is a control volume since mass crosses the boundary. There is only one inlet and one exit, and thus . The energy balance for this adiabatic steady-flow system can be expressed in the rate form as

Thus,

6-112 A house is heated by an electric resistance heater placed in a duct. The power rating of the electric heater is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Air is an ideal gas with constant specific heats at room temperature. 3 Kinetic and potential energy changes are negligible.

Properties The constant pressure specific heat of air at room temperature is cp = 1.005 kJ/kg·K (Table A-2)

Analysis We take the heating duct as the system, which is a control volume since mass crosses the boundary. There is only one inlet and one exit, and thus . The energy balance for this steady-flow system can be expressed in the rate form as

Substituting, the power rating of the heating element is determined to be

6-113 A hair dryer consumes 1200 W of electric power when running. The inlet volume flow rate and the exit velocity of air are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Air is an ideal gas with constant specific heats at room temperature. 3 Kinetic and potential energy changes are negligible. 4 The power consumed by the fan and the heat losses are negligible.

Properties The gas constant of air is 0.287 kPa.m3/kg.K (Table A-1). The constant pressure specific heat of air at room temperature is cp = 1.005 kJ/kg·K (Table A-2)

Analysis We take the hair dryer as the system, which is a control volume since mass crosses the boundary. There is only one inlet and one exit, and thus . The energy balance for this steady-flow system can be expressed in the rate form as

Substituting, the mass and volume flow rates of air are determined to be

(b) The exit velocity of air is determined from the mass balance  to be

6-114 EES Problem 6-113 is reconsidered. The effect of the exit cross-sectional area of the hair drier on the exit velocity as the exit area varies from 25 cm2 to 75 cm2 is to be investigated. The exit velocity is to be plotted against the exit cross-sectional area.

Analysis The problem is solved using EES, and the results are tabulated and plotted below.

"Knowns:"

R=0.287 [kPa-m^3/kg-K]

P= 100 [kPa]

T_1 = 22 [C]

T_2= 47 [C]

{A_2 = 60 [cm^2]}

A_1 = 53.35 [cm^2]

W_dot_ele=1200 [W]

"Analysis:

We take the hair dryer as the system, which is a control volume since mass crosses the boundary. There is only one inlet and one exit.  Thus, the energy balance for this steady-flow system can be expressed in the rate form as:"

E_dot_in = E_dot_out

E_dot_in = W_dot_ele*convert(W,kW) + m_dot_1*(h_1+Vel_1^2/2*convert(m^2/s^2,kJ/kg))

E_dot_out = m_dot_2*(h_2+Vel_2^2/2*convert(m^2/s^2,kJ/kg))

h_2  = enthalpy(air, T = T_2)

h_1= enthalpy(air, T = T_1)

"The volume flow rates of air are determined to be:"

V_dot_1 = m_dot_1*v_1

P*v_1=R*(T_1+273)

V_dot_2 = m_dot_2*v_2

P*v_2=R*(T_2+273)

m_dot_1 = m_dot_2

Vel_1=V_dot_1/(A_1*convert(cm^2,m^2))

"(b) The exit velocity of air is determined from the mass balance  to be"

Vel_2=V_dot_2/(A_2*convert(cm^2,m^2))

| A2 [cm2] | Vel2 [m/s] |
| --- | --- |
| 25 | 16 |
| 30 | 13.75 |
| 35 | 12.03 |
| 40 | 10.68 |
| 45 | 9.583 |
| 50 | 8.688 |
| 55 | 7.941 |
| 60 | 7.31 |
| 65 | 6.77 |
| 70 | 6.303 |
| 75 | 5.896 |

6-115 The ducts of a heating system pass through an unheated area. The rate of heat loss from the air in the ducts is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Air is an ideal gas with constant specific heats at room temperature. 3 Kinetic and potential energy changes are negligible. 4 There are no work interactions involved.

Properties The constant pressure specific heat of air at room temperature is cp = 1.005 kJ/kg·K (Table A-2)

Analysis We take the heating duct as the system, which is a control volume since mass crosses the boundary. There is only one inlet and one exit, and thus . The energy balance for this steady-flow system can be expressed in the rate form as

Substituting,

6-116 Steam pipes pass through an unheated area, and the temperature of steam drops as a result of heat losses. The mass flow rate of steam and the rate of heat loss from are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time.  2 Kinetic and potential energy changes are negligible. 4 There are no work interactions involved.

Properties From the steam tables (Table A-6),

Analysis (a) The mass flow rate of steam is determined directly from

(b) We take the steam pipe as the system, which is a control volume since mass crosses the boundary. There is only one inlet and one exit, and thus . The energy balance for this steady-flow system can be expressed in the rate form as

Substituting, the rate of heat loss is determined to be

6-117 Steam flows through a non-constant cross-section pipe. The inlet and exit velocities of the steam are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Potential energy change is negligible. 3 There are no work interactions. 4 The device is adiabatic and thus heat transfer is negligible.

Analysis We take the pipe as the system, which is a control volume since mass crosses the boundary. The mass and energy balances for this steady-flow system can be expressed in the rate form as

Mass balance:

Energy balance:

The properties of steam at the inlet and exit are (Table A-6)

Assuming inlet diameter to be 1.8 m and the exit diameter to be 1.0 m, and substituting,

(1)

(2)

There are two equations and two unknowns. Solving equations (1) and (2) simultaneously using an equation solver such as EES, the velocities are determined to be

V1 = 118.8 m/s

V2 = 458.0 m/s

6-118E Saturated liquid water is heated in a steam boiler. The heat transfer per unit mass is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions.

Analysis We take the pipe in which the water is heated as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

The enthalpies of water at the inlet and exit of the boiler are (Table A-5E, A-6E).

Substituting,

6-119 R-134a is condensed in a condenser. The heat transfer per unit mass is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions.

Analysis We take the pipe in which R-134a is condensed as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

The enthalpies of R-134a at the inlet and exit of the condenser are (Table A-12, A-13).

Substituting,

6-120 Water is heated at constant pressure so that it changes a state from saturated liquid to saturated vapor. The heat transfer per unit mass is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions.

Analysis We take the pipe in which water is heated as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

where		(Table A-5)

Thus,

Charging and Discharging Processes

6-121 Helium flows from a supply line to an initially evacuated tank. The flow work of the helium in the supply line and the final temperature of the helium in the tank are to be determined.

Properties The properties of helium are R = 2.0769 kJ/kg.K, cp = 5.1926 kJ/kg.K, cv = 3.1156 kJ/kg.K (Table A-2a).

Analysis The flow work is determined from its definition but we first determine the specific volume

Noting that the flow work in the supply line is converted to sensible internal energy in the tank, the final helium temperature in the tank is determined as follows

Alternative Solution: Noting the definition of specific heat ratio, the final temperature in the tank can also be determined from

which is practically the same result.

6-122 An evacuated bottle is surrounded by atmospheric air. A valve is opened, and air is allowed to fill the bottle. The amount of heat transfer through the wall of the bottle when thermal and mechanical equilibrium is established is to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the inlet remains constant. 2 Air is an ideal gas with variable specific heats. 3 Kinetic and potential energies are negligible. 4 There are no work interactions involved. 5 The direction of heat transfer is to the air in the bottle (will be verified).

Properties The gas constant of air is 0.287 kPa.m3/kg.K (Table A-1).

Analysis We take the bottle as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Combining the two balances:

where

Substituting,

Qin = (0.0096 kg)(206.91 - 290.16) kJ/kg = - 0.8 kJ

or

Qout = 0.8 kJ

Discussion The negative sign for heat transfer indicates that the assumed direction is wrong. Therefore, we reverse the direction.

6-123 An insulated rigid tank is evacuated. A valve is opened, and air is allowed to fill the tank until mechanical equilibrium is established. The final temperature in the tank is to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the inlet remains constant. 2 Air is an ideal gas with constant specific heats. 3 Kinetic and potential energies are negligible. 4 There are no work interactions involved. 5 The device is adiabatic and thus heat transfer is negligible.

Properties The specific heat ratio for air at room temperature is  k = 1.4 (Table A-2).

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Combining the two balances:

Substituting,

6-124 A rigid tank initially contains air at atmospheric conditions. The tank is connected to a supply line, and air is allowed to enter the tank until mechanical equilibrium is established. The mass of air that entered and the amount of heat transfer are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the inlet remains constant. 2 Air is an ideal gas with variable specific heats. 3 Kinetic and potential energies are negligible. 4 There are no work interactions involved. 5 The direction of heat transfer is to the tank (will be verified).

Properties The gas constant of air is 0.287 kPa.m3/kg.K (Table A-1). The properties of air are (Table A-21)

Analysis (a) We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

The initial and the final masses in the tank are

Then from the mass balance,

(b) The heat transfer during this process is determined from

Discussion The negative sign for heat transfer indicates that the assumed direction is wrong. Therefore, we reversed the direction.

6-125 A rigid tank initially contains saturated R-134a liquid-vapor mixture. The tank is connected to a supply line, and R-134a is allowed to enter the tank. The final temperature in the tank, the mass of R-134a that entered, and the heat transfer are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the inlet remains constant.  2 Kinetic and potential energies are negligible. 3 There are no work interactions involved. 4 The direction of heat transfer is to the tank (will be verified).

Properties The properties of refrigerant are (Tables A-11 through A-13)

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

(a) The tank contains saturated vapor at the final state at 800 kPa, and thus the final temperature is the saturation temperature at this pressure,

31.31ºC

(b)  The initial and the final masses in the tank are

Then from the mass balance

2.43 kg

(c)  The heat transfer during this process is determined from the energy balance to be

6-126 A cylinder initially contains saturated liquid-vapor mixture of water. The cylinder is connected to a supply line, and the steam is allowed to enter the cylinder until all the liquid is vaporized. The final temperature in the cylinder and the mass of the steam that entered are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the inlet remains constant.  2 The expansion process is quasi-equilibrium.  3 Kinetic and potential energies are negligible. 3 There are no work interactions involved other than boundary work. 4 The device is insulated and thus heat transfer is negligible.

Properties The properties of steam are (Tables A-4 through A-6)

Analysis (a) The cylinder contains saturated vapor at the final state at a pressure of 200 kPa, thus the final temperature in the cylinder must be

T2 = Tsat @ 200 kPa = 120.2°C

(b) We take the cylinder as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Combining the two relations gives

or,

since the boundary work and (U combine into (H for constant pressure expansion and compression processes. Solving for m2 and substituting,

Thus,

mi = m2 - m1 = 29.07 - 10 = 19.07 kg

6-127E A scuba diver's air tank is to be filled with air from a compressed air line. The temperature and mass in the tank at the final state are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the inlet remains constant. 2 Air is an ideal gas with constant specific heats. 3 Kinetic and potential energies are negligible. 4 There are no work interactions involved. 5 The tank is well-insulated, and thus there is no heat transfer.

Properties The gas constant of air is 0.3704 psia·ft3/lbm·R (Table A-1E). The specific heats of air at room temperature are cp = 0.240 Btu/lbm·R and cv = 0.171 Btu/lbm·R (Table A-2Ea).

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Combining the two balances:

The initial and final masses are given by

Substituting,

whose solution is

The final mass is then

6-128 R-134a from a tank is discharged to an air-conditioning line in an isothermal process. The final quality of the R-134a in the tank and the total heat transfer are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the exit remains constant. 2 Kinetic and potential energies are negligible. 3 There are no work interactions involved.

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Combining the two balances:

The initial state properties of R-134a in the tank are

(Table A-11)

Note that we assumed that the refrigerant leaving the tank is at saturated liquid state, and found the exiting enthalpy accordingly. The volume of the tank is

The final specific volume in the container is

The final state is now fixed. The properties at this state are (Table A-11)

Substituting into the energy balance equation,

6-129E Oxygen is supplied to a medical facility from 10 compressed oxygen tanks in an isothermal process. The mass of oxygen used and the total heat transfer to the tanks are to be determined.

Assumptions 1 This is an unsteady process but it can be analyzed as a uniform-flow process. 2 Oxygen is an ideal gas with constant specific heats. 3 Kinetic and potential energies are negligible. 4 There are no work interactions involved.

Properties The gas constant of oxygen is 0.3353 psia·ft3/lbm·R (Table A-1E). The specific heats of oxygen at room temperature are cp = 0.219 Btu/lbm·R and cv = 0.157 Btu/lbm·R (Table A-2Ea).

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Combining the two balances:

The initial and final masses, and the mass used are

Substituting into the energy balance equation,

6-130 The air in an insulated, rigid compressed-air tank is released until the pressure in the tank reduces to a specified value. The final temperature of the air in the tank is to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process. 2 Air is an ideal gas with constant specific heats. 3 Kinetic and potential energies are negligible. 4 There are no work interactions involved. 5 The tank is well-insulated, and thus there is no heat transfer.

Properties The gas constant of air is 0.287 kPa·m3/kg·K (Table A-1). The specific heats of air at room temperature are cp = 1.005 kJ/kg·K and cv = 0.718 kJ/kg·K (Table A-2a).

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Combining the two balances:

The initial and final masses are given by

The temperature of air leaving the tank changes from the initial temperature in the tank to the final temperature during the discharging process. We assume that the temperature of the air leaving the tank is the average of initial and final temperatures in the tank. Substituting into the energy balance equation gives

whose solution by trial-error or by an equation solver such as EES is

6-131E Steam is supplied from a line to a weighted piston-cylinder device. The final temperature (and quality if appropriate) of the steam in the piston cylinder and the total work produced as the device is filled are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the inlet remains constant. 2 Kinetic and potential energies are negligible. 3 The process is adiabatic.

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, and also noting that the initial mass in the system is zero, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Combining the two balances:

The boundary work is determined from

Substituting, the energy balance equation simplifies into

The enthalpy of steam at the inlet is

Substituting this value into the energy balance equation and using an iterative solution of this equation gives (or better yet using EES software)

The final mass is

and the work produced is

6-132E Oxygen is supplied from a line to a weighted piston-cylinder device. The final temperature of the oxygen in the piston cylinder and the total work produced as the device is filled are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the inlet remains constant. 2 Kinetic and potential energies are negligible. 3 The process is adiabatic. 4 Oxygen is an ideal gas with constant specific heats.

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, and also noting that the initial mass in the system is zero, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Combining the two balances:

The boundary work is determined from

Substituting, the energy balance equation simplifies into

Solving for the final temperature,

The work produced is

6-133 A rigid tank initially contains saturated R-134a vapor. The tank is connected to a supply line, and R-134a is allowed to enter the tank. The mass of the R-134a that entered and the heat transfer are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the inlet remains constant.  2 Kinetic and potential energies are negligible. 3 There are no work interactions involved. 4 The direction of heat transfer is to the tank (will be verified).

Properties The properties of refrigerant are (Tables A-11 through A-13)

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

(a)  The initial and the final masses in the tank are

Then from the mass balance

(c)  The heat transfer during this process is determined from the energy balance to be

6-134 A rigid tank initially contains saturated liquid water. A valve at the bottom of the tank is opened, and half of the mass in liquid form is withdrawn from the tank. The temperature in the tank is maintained constant.  The amount of heat transfer is to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid leaving the device remains constant.  2 Kinetic and potential energies are negligible. 3 There are no work interactions involved. 4 The direction of heat transfer is to the tank (will be verified).

Properties The properties of water are (Tables A-4 through A-6)

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

The initial and the final masses in the tank are

Then from the mass balance,

Now we determine the final internal energy,

Then the heat transfer during this process is determined from the energy balance by substitution to be

6-135 A rigid tank initially contains saturated liquid-vapor mixture of refrigerant-134a. A valve at the bottom of the tank is opened, and liquid is withdrawn from the tank at constant pressure until no liquid remains inside. The amount of heat transfer is to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid leaving the device remains constant.  2 Kinetic and potential energies are negligible. 3 There are no work interactions involved. 4 The direction of heat transfer is to the tank (will be verified).

Properties The properties of R-134a are (Tables A-11 through A-13)

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

The initial mass, initial internal energy, and final mass in the tank are

Then from the mass and energy balances,

6-136E A rigid tank initially contains saturated liquid-vapor mixture of R-134a. A valve at the top of the tank is opened, and vapor is allowed to escape at constant pressure until all the liquid in the tank disappears.  The amount of heat transfer is to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid leaving the device remains constant.  2 Kinetic and potential energies are negligible. 3 There are no work interactions involved.

Properties The properties of R-134a are (Tables A-11E through A-13E)

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

The initial mass, initial internal energy, and final mass in the tank are

Then from the mass and energy balances,

6-137 A rigid tank initially contains superheated steam. A valve at the top of the tank is opened, and vapor is allowed to escape at constant pressure until the temperature rises to 500(C.  The amount of heat transfer is to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process by using constant average properties for the steam leaving the tank.  2 Kinetic and potential energies are negligible. 3 There are no work interactions involved. 4 The direction of heat transfer is to the tank (will be verified).

Properties The properties of water are (Tables A-4 through A-6)

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

The state and thus the enthalpy of the steam leaving the tank is changing during this process.  But for simplicity, we assume constant properties for the exiting steam at the average values. Thus,

The initial and the final masses in the tank are

Then from the mass and energy balance relations,

6-138 Steam is supplied from a line to a piston-cylinder device equipped with a spring. The final temperature (and quality if appropriate) of the steam in the cylinder and the total work produced as the device is filled are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the inlet remains constant. 2 Kinetic and potential energies are negligible. 3 The process is adiabatic.

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, and also noting that the initial mass in the system is zero, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Combining the two balances:

Because of the spring, the relation between the pressure and volume is a linear relation. According to the data in the problem statement,

The final vapor volume is then

The work needed to compress the spring is

The enthalpy of steam at the inlet is

Substituting the information found into the energy balance equation gives

Using an iterative solution of this equation with steam tables gives (or better yet using EES software)

6-139 Air is supplied from a line to a piston-cylinder device equipped with a spring. The final temperature of the steam in the cylinder and the total work produced as the device is filled are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the inlet remains constant. 2 Kinetic and potential energies are negligible. 3 The process is adiabatic. 4 Air is an ideal gas with constant specific heats.

Properties The gas constant of air is 0.287 kPa·m3/kg·K (Table A-1). The specific heats of air at room temperature are cp = 1.005 kJ/kg·K and cv = 0.718 kJ/kg·K (Table A-2a).

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, and also noting that the initial mass in the system is zero, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Combining the two balances:

Because of the spring, the relation between the pressure and volume is a linear relation. According to the data in the problem statement,

The final air volume is then

The work needed to compress the spring is

Substituting the information found into the energy balance equation gives

The final temperature is then

6-140 A hot-air balloon is considered. The final volume of the balloon and work produced by the air inside the balloon as it expands the balloon skin are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process. 2 Air is an ideal gas with constant specific heats. 3 Kinetic and potential energies are negligible. 4 There is no heat transfer.

Properties The gas constant of air is 0.287 kPa·m3/kg·K (Table A-1).

Analysis The specific volume of the air at the entrance and exit, and in the balloon is

The mass flow rate at the entrance is then

while that at the outlet is

Applying a mass balance to the balloon,

The volume in the balloon then changes by the amount

and the final volume of the balloon is

In order to push back the boundary of the balloon against the surrounding atmosphere, the amount of work that must be done is

6-141 An insulated rigid tank initially contains helium gas at high pressure. A valve is opened, and half of the mass of helium is allowed to escape. The final temperature and pressure in the tank are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process by using constant average properties for the helium leaving the tank.  2 Kinetic and potential energies are negligible. 3 There are no work interactions involved. 4 The tank is insulated and thus heat transfer is negligible. 5 Helium is an ideal gas with constant specific heats.

Properties The specific heat ratio of helium is k =1.667 (Table A-2).

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Note that the state and thus the enthalpy of helium leaving the tank is changing during this process.  But for simplicity, we assume constant properties for the exiting steam at the average values.

Combining the mass and energy balances:

Dividing by m1/2

Dividing by cv:

Solving for T2:

The final pressure in the tank is

6-142E An insulated rigid tank equipped with an electric heater initially contains pressurized air. A valve is opened, and air is allowed to escape at constant temperature until the pressure inside drops to 30 psia. The  amount of electrical work transferred is to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the exit temperature (and enthalpy) of air remains constant.  2 Kinetic and potential energies are negligible. 3 The tank is insulated and thus heat transfer is negligible. 4 Air is an ideal gas with variable specific heats.

Properties The gas constant of air is R =0.3704 psia.ft3/lbm.R (Table A-1E). The properties of air are (Table A-21E)

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

The initial and the final masses of air in the tank are

Then from the mass and energy balances,

6-143 A vertical cylinder initially contains air at room temperature. Now a valve is opened, and air is allowed to escape at constant pressure and temperature until the volume of the cylinder goes down by half. The  amount air that left the cylinder and the amount of heat transfer are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the exit temperature (and enthalpy) of air remains constant.  2 Kinetic and potential energies are negligible. 3 There are no work interactions other than boundary work. 4 Air is an ideal gas with constant specific heats. 5 The direction of heat transfer is to the cylinder (will be verified).

Properties The gas constant of air is R = 0.287 kPa.m3/kg.K (Table A-1).

Analysis (a) We take the cylinder as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

The initial and the final masses of air in the cylinder are

Then from the mass balance,

(b) This is a constant pressure process, and thus the Wb and the (U terms can be combined into (H to yield

Noting that the temperature of the air remains constant during this process, we have

hi = h1 = h2 = h.

Also,

.

Thus,

6-144 A balloon is initially filled with helium gas at atmospheric conditions. The tank is connected to a supply line, and helium is allowed to enter the balloon until the pressure rises from 100 to 150 kPa. The final temperature in the balloon is to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the inlet remains constant. 2 Helium is an ideal gas with constant specific heats. 3 The expansion process is quasi-equilibrium.  4 Kinetic and potential energies are negligible. 5 There are no work interactions involved other than boundary work. 6 Heat transfer is negligible.

Properties The gas constant of helium is R = 2.0769 kJ/kg·K (Table A-1). The specific heats of helium are cp = 5.1926 and cv = 3.1156 kJ/kg·K (Table A-2a).

Analysis  We take the cylinder as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Then from the mass balance,

Noting that P varies linearly with V, the boundary work done during this process is

Using specific heats, the energy balance relation reduces to

Substituting,

It yields		T2 = 333.6 K

6-145 An insulated piston-cylinder device with a linear spring is applying force to the piston. A valve at the bottom of the cylinder is opened, and refrigerant is allowed to escape. The amount of refrigerant that escapes and the final temperature of the refrigerant are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process assuming that the state of fluid leaving the device remains constant. 2 Kinetic and potential energies are negligible.

Properties The initial properties of R-134a are (Tables A-11 through A-13)

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

The initial mass and the relations for the final and exiting masses are

Noting that the spring is linear, the boundary work can be determined from

Substituting the energy balance,

(Eq. 1)

where the enthalpy of exiting fluid is assumed to be the average of initial and final enthalpies of the refrigerant in the cylinder. That is,

Final state properties of the refrigerant (h2, u2, and v2) are all functions of final pressure (known) and temperature (unknown). The solution may be obtained by a trial-error approach by trying different final state temperatures until Eq. (1) is satisfied. Or solving the above equations simultaneously using an equation solver with built-in thermodynamic functions such as EES, we obtain

T2 = 96.8(C,  me = 22.47 kg, h2 = 336.20 kJ/kg,

u2 = 307.77 kJ/kg, v2 = 0.04739 m3/kg, m2 = 10.55 kg

6-146 Steam at a specified state is allowed to enter a piston-cylinder device in which steam undergoes a constant pressure expansion process. The amount of mass that enters and the amount of heat transfer are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid entering the device remains constant. 2 Kinetic and potential energies are negligible.

Properties The properties of steam at various states are (Tables A-4 through A-6)

Analysis (a) We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Noting that the pressure remains constant, the boundary work is determined from

The final mass and the mass that has entered are

(b) Finally, substituting into energy balance equation

Review Problems

6-147 A water tank open to the atmosphere is initially filled with water. The tank discharges to the atmosphere through a long pipe connected to a valve. The initial discharge velocity from the tank and the time required to empty the tank are to be determined.

Assumptions 1 The flow is incompressible. 2 The draining pipe is horizontal. 3 The tank is considered to be empty when the water level drops to the center of the valve.

Analysis (a) Substituting the known quantities, the discharge velocity can be expressed as

Then the initial discharge velocity becomes

where z is the water height relative to the center of the orifice at that time.

(b) The flow rate of water from the tank can be obtained by multiplying the discharge velocity by the pipe cross-sectional area,

Then the amount of water that flows through the pipe during a differential time interval dt is

(1)

which, from conservation of mass, must be equal to the decrease in the volume of water in the tank,

(2)

where dz is the change in the water level in the tank during dt. (Note that dz is a negative quantity since the positive direction of z is upwards. Therefore, we used –dz to get a positive quantity for the amount of water discharged). Setting Eqs. (1) and (2) equal to each other and rearranging,

The last relation can be integrated easily since the variables are separated. Letting tf be the discharge time and integrating it from t = 0 when z = z1 to t = tf when z = 0 (completely drained tank) gives

Simplifying and substituting the values given, the draining time is determined to be

Discussion The draining time can be shortened considerably by installing a pump in the pipe.

6-148 The rate of accumulation of water in a pool and the rate of discharge are given. The rate supply of water to the pool is to be determined.

Assumptions 1 Water is supplied and discharged steadily. 2 The rate of evaporation of water is negligible. 3 No water is supplied or removed through other means.

Analysis The conservation of mass principle applied to the pool requires that the rate of increase in the amount of water in the pool be equal to the difference between the rate of supply of water and the rate of discharge. That is,

since the density of water is constant and thus the conservation of mass is equivalent to conservation of volume. The rate of discharge of water is

The rate of accumulation of water in the pool is equal to the cross-section of the pool times the rate at which the water level rises,

Substituting, the rate at which water is supplied to the pool is determined to be

Therefore, water is supplied at a rate of 0.01282 m3/s = 12.82 L/s.

6-149  A fluid is flowing in a circular pipe. A relation is to be obtained for the average fluid velocity in therms of V(r), R, and r.

Analysis Choosing a circular ring of area dA = 2(rdr as our differential area, the mass flow rate through a cross-sectional area can be expressed as

Solving for Vavg,

6-150 Air is accelerated in a nozzle. The density of air at the nozzle exit is to be determined.

Assumptions Flow through the nozzle is steady.

Properties The density of air is given to be 4.18 kg/m3 at the inlet.

Analysis  There is only one inlet and one exit, and thus . Then,

Discussion Note that the density of air decreases considerably despite a decrease in the cross-sectional area of the nozzle.

6-151 An air compressor consumes 4.5 kW of power to compress a specified rate of air. The flow work required by the compressor is to be compared to the power used to increase the pressure of the air.

Assumptions 1 Flow through the compressor is steady. 2 Air is an ideal gas.

Properties The gas constant of air is 0.287 kPa·m3/kg·K (Table A-1).

Analysis The specific volume of the air at the inlet is

The mass flow rate of the air is

Combining the flow work expression with the ideal gas equation of state gives the flow work as

The flow power is

The remainder of compressor power input is used to increase the pressure of the air:

6-152 Steam expands in a turbine whose power production is 9000 kW. The rate of heat lost from the turbine is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible.

Properties From the steam tables (Tables A-6 and A-4)

Analysis We take the turbine as the system, which is a control volume since mass crosses the boundary. Noting that there is one inlet and one exiti the energy balance for this steady-flow system can be expressed in the rate form as

Substituting,

6-153E Nitrogen gas flows through a long, constant-diameter adiabatic pipe. The velocities at the inlet and exit are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Nitrogen is an ideal gas with constant specific heats. 3 Potential energy changes are negligible. 4 There are no work interactions. 5 The re is no heat transfer from the nitrogen.

Properties The specific heat of nitrogen at the room temperature iss cp = 0.248 Btu/lbm(R (Table A-2Ea).

Analysis There is only one inlet and one exit, and thus . We take the pipe as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Combining the mass balance and ideal gas equation of state yields

Substituting this expression for V2 into the energy balance equation gives

The velocity at the exit is

6-154 Water at a specified rate is heated by an electrical heater. The current is to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 The heat losses from the water is negligible.

Properties The specific heat and the density of water are taken to be cp = 4.18 kJ/kg·°C and ( = 1 kg/L (Table A-3).

Analysis We take the pipe in which water is heated as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

The mass flow rate of the water is

Substituting into the energy balance equation and solving for the current gives

6-155 Steam flows in an insulated pipe. The mass flow rate of the steam and the speed of the steam at the pipe outlet are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work and heat interactions.

Analysis We take the pipe in which steam flows as the system, which is a control volume. The energy balance for this steady-flow system can be expressed in the rate form as

The properties of the steam at the inlet and exit are (Table A-6)

The mass flow rate is

The outlet velocity will then be

6-156 The mass flow rate of a compressed air line is divided into two equal streams by a T-fitting in the line. The velocity of the air at the outlets and the rate of change of flow energy (flow power) across the T-fitting are to be determined.

Assumptions 1 Air is an ideal gas with constant specific heats. 2 The flow is steady. 3 Since the outlets are identical, it is presumed that the flow divides evenly between the two.

Properties The gas constant of air is R = 0.287 kPa(m3/kg(K (Table A-1).

Analysis  The specific volumes of air at the inlet and outlets are

Assuming an even division of the inlet flow rate, the mass balance can be written as

The mass flow rate at the inlet is

while that at the outlets is

Substituting the above results into the flow power expression produces

6-157 Air flows through a non-constant cross-section pipe. The inlet and exit velocities of the air are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Potential energy change is negligible. 3 There are no work interactions. 4 The device is adiabatic and thus heat transfer is negligible. 5 Air is an ideal gas with constant specific heats.

Properties The gas constant of air is R = 0.287 kPa.m3/kg.K. Also, cp = 1.005 kJ/kg.K for air at room temperature (Table A-2)

Analysis We take the pipe as the system, which is a control volume since mass crosses the boundary. The mass and energy balances for this steady-flow system can be expressed in the rate form as

Mass balance:

Energy balance:

or

Assuming inlet diameter to be 1.8 m and the exit diameter to be 1.0 m, and substituting given values into mass and energy balance equations

(1)

(2)

There are two equations and two unknowns. Solving equations (1) and (2) simultaneously using an equation solver such as EES, the velocities are determined to be

V1 = 28.6 m/s

V2 = 120 m/s

6-158  Cold water enters a steam generator at 20(C, and leaves as saturated vapor at Tsat = 150C. The fraction of heat used to preheat the liquid water from 20(C to saturation temperature of 150(C is to be determined.

Assumptions  1 Steady operating conditions exist. 2 Heat losses from the steam generator are negligible. 3 The specific heat of water is constant at the average temperature.

Properties   The heat of vaporization of water at 150C is hfg = 2113.8 kJ/kg (Table A-4), and the specific heat of liquid water is c = 4.18 kJ/kg.(C (Table A-3).

Analysis The heat of vaporization of water represents the amount of heat needed to vaporize a unit mass of liquid at a specified temperature. Using the average specific heat, the amount of heat transfer needed to preheat a unit mass of water from 20(C to 150(C is

and

Therefore, the fraction of heat used to preheat the water is

6-159  Cold water enters a steam generator at 20(C and is boiled, and leaves as saturated vapor at boiler pressure. The boiler pressure at which the amount of heat needed to preheat the water to saturation temperature that is equal to the heat of vaporization is to be determined.

Assumptions  Heat losses from the steam generator are negligible.

Properties  The enthalpy of liquid water at 20(C is 83.91 kJ/kg. Other properties needed to solve this problem are the heat of vaporization hfg and the enthalpy of saturated liquid at the specified temperatures, and they can be obtained from Table A-4.

Analysis The heat of vaporization of water represents the amount of heat needed to vaporize a unit mass of liquid at a specified temperature, and (h represents the amount of heat needed to preheat a unit mass of water from 20(C to the saturation temperature. Therefore,

The solution of this problem requires choosing a boiling temperature, reading hf and hfg at that temperature, and substituting the values into the relation above to see if it is satisfied. By trial and error,  (Table A-4)

At 310(C:    1402.0 – 1325.9 = 76.1 kJ/kg

At 315(C:    1431.6 – 1283.4 = 148.2 kJ/kg

The temperature that satisfies this condition is determined from the two values above by interpolation to be 310.6(C. The saturation pressure corresponding to this temperature is 9.94 MPa.

6-160E A refrigeration system is to cool eggs by chilled air at a rate of 10,000 eggs per hour. The rate of heat removal from the eggs, the required volume flow rate of air, and the size of the compressor of the refrigeration system are to be determined.

Assumptions 1 Steady operating conditions exist. 2 The eggs are at uniform temperatures before and after cooling. 3 The cooling section is well-insulated. 4 The properties of eggs are constant. 5 The local atmospheric pressure is 1 atm.

Properties The properties of the eggs are given to ( = 67.4 lbm/ft3 and cp = 0.80 Btu/lbm.(F. The specific heat of air at room temperature cp = 0.24 Btu/lbm. (F (Table A-2E). The gas constant of air is R = 0.3704 psia.ft3/lbm.R (Table A-1E).

Analysis   (a) Noting that eggs are cooled at a rate of 10,000 eggs per hour, eggs can be considered to flow steadily through the cooling section at a mass flow rate of

Taking the egg flow stream in the cooler as the system, the energy balance for steadily flowing eggs can be expressed in the rate form as

Then the rate of heat removal from the eggs as they are cooled from 90(F to 50ºF at this rate becomes

(b) All the heat released by the eggs is absorbed by the refrigerated air since heat transfer through he walls of cooler is negligible, and the temperature rise of air is not to exceed 10(F.  The minimum mass flow and volume flow rates of air are determined to be

6-161  Glass bottles are washed in hot water in an uncovered rectangular glass washing bath. The   rates of heat and water mass that need to be supplied to the water are to be determined.

Assumptions 1 Steady operating conditions exist. 2 The entire water body is maintained at a uniform temperature of 55(C. 3 Heat losses from the outer surfaces of the bath are negligible. 4 Water is an incompressible substance with constant properties.

Properties The specific heat of water at room temperature is cp = 4.18 kJ/kg.(C. Also, the specific heat of glass is 0.80 kJ/kg.(C (Table A-3).

Analysis (a) The mass flow rate of glass bottles through the water bath in steady operation is

Taking the bottle flow section as the system, which is a steady-flow control volume, the energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat removal by the bottles as they are heated from 20 to 55(C is

The amount of water removed by the bottles is

Noting that the water removed by the bottles is made up by fresh water entering

at 15(C, the rate of heat removal by the water that sticks to the bottles is

Therefore, the total amount of heat removed by the wet bottles is

Discussion In practice, the rates of heat and water removal will be much larger since the heat losses from the tank and the moisture loss from the open surface are not considered.

6-162  Glass bottles are washed in hot water in an uncovered rectangular glass washing bath. The   rates of heat and water mass that need to be supplied to the water are to be determined.

Assumptions 1 Steady operating conditions exist. 2 The entire water body is maintained at a uniform temperature of 50(C. 3 Heat losses from the outer surfaces of the bath are negligible. 4 Water is an incompressible substance with constant properties.

Properties The specific heat of water at room temperature is cp = 4.18 kJ/kg.(C. Also, the specific heat of glass is 0.80 kJ/kg.(C (Table A-3).

Analysis (a) The mass flow rate of glass bottles through the water bath in steady operation is

Taking the bottle flow section as the system, which is a steady-flow control volume, the energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat removal by the bottles as they are heated from 20 to 50(C is

The amount of water removed by the bottles is

Noting that the water removed by the bottles is made up by fresh water entering at 15(C, the rate of heat removal by the water that sticks to the bottles is

Therefore, the total amount of heat removed by the wet bottles is

Discussion In practice, the rates of heat and water removal will be much larger since the heat losses from the tank and the moisture loss from the open surface are not considered.

6-163 Long aluminum wires are extruded at a velocity of 10 m/min, and are exposed to atmospheric air. The rate of heat transfer from the wire is to be determined.

Assumptions 1 Steady operating conditions exist.  2 The thermal properties of the wire are constant.

Properties The properties of aluminum are given to be ( = 2702 kg/m3 and cp = 0.896 kJ/kg.(C.

Analysis  The mass flow rate of the extruded wire through the air is

Taking the volume occupied by the extruded wire as the system, which is a steady-flow control volume, the energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat transfer from the wire to the air becomes

6-164 Long copper wires are extruded at a velocity of 10 m/min, and are exposed to atmospheric air. The rate of heat transfer from the wire is to be determined.

Assumptions 1 Steady operating conditions exist.  2 The thermal properties of the wire are constant.

Properties The properties of copper are given to be ( = 8950 kg/m3 and cp = 0.383 kJ/kg.(C.

Analysis  The mass flow rate of the extruded wire through the air is

Taking the volume occupied by the extruded wire as the system, which is a steady-flow control volume, the energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat transfer from the wire to the air becomes

6-165 Steam at a saturation temperature of Tsat = 40C condenses on the outside of a thin horizontal tube. Heat is transferred to the cooling water that enters the tube at 25C and exits at 35C. The rate of condensation of steam is to be determined.

Assumptions  1 Steady operating conditions exist. 2 Water is an incompressible substance with constant properties at room temperature. 3 The changes in kinetic and potential energies are negligible.

Properties   The properties of water at room temperature are ( = 997 kg/m3 and cp = 4.18 kJ/kg.(C (Table A-3). The enthalpy of vaporization of water at 40C is hfg = 2406.0 kJ/kg (Table A-4).

Analysis The mass flow rate of water through the tube is

Taking the volume occupied by the cold water in the tube as the system, which is a steady-flow control volume, the energy balance for this steady-flow system can be expressed in the rate form as

Then the rate of heat transfer to the water and the rate of condensation become

6-166 A fan is powered by a 0.5 hp motor, and delivers air at a rate of 85 m3/min. The highest possible air velocity at the fan exit is to be determined.

Assumptions  1 This is a steady-flow process since there is no change with time at any point and thus . 2 The inlet velocity and the change in potential energy are negligible, .  3 There are no heat and work interactions other than the electrical power consumed by the fan motor. 4 The efficiencies of the motor and the fan are 100% since best possible operation is assumed. 5 Air is an ideal gas with constant specific heats at room temperature.

Properties  The density of air is given to be ( = 1.18 kg/m3. The constant pressure specific heat of air at room temperature is cp = 1.005 kJ/kg.(C (Table A-2).

Analysis We take the fan-motor assembly as the system. This is a control volume since mass crosses the system boundary during the process. We note that there is only one inlet and one exit, and thus .

The velocity of air leaving the fan will be highest when all of the entire electrical energy drawn by the motor is converted to kinetic energy, and the friction between the air layers is zero. In this best possible case, no energy will be converted to thermal energy, and thus the temperature change of air will be zero,  Then the energy balance for this steady-flow system can be expressed in the rate form as

Noting that the temperature and thus enthalpy remains constant, the relation above simplifies further to

where

Solving for V2 and substituting gives

Discussion In reality, the velocity will be less because of the inefficiencies of the motor and the fan.

6-167 A tank initially contains saturated mixture of R-134a. A valve is opened and R-134a vapor only is allowed to escape slowly such that temperature remains constant. The heat transfer necessary with the surroundings to maintain the temperature and pressure of the R-134a constant is to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the exit remains constant. 2 Kinetic and potential energies are negligible. 3 There are no work interactions involved.

Analysis We take the tank as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Combining the two balances:

The specific volume at the initial state is

The initial state properties of R-134a in the tank are

(Table A-11)

The enthalpy of saturated vapor refrigerant leaving the bottle is

The specific volume at the final state is

The internal energy at the final state is

(Table A-11)

Substituting into the energy balance equation,

6-168 CD EES Steam expands in a turbine steadily. The mass flow rate of the steam, the exit velocity, and the power output are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Potential energy changes are negligible.

Properties From the steam tables (Tables A-4 through 6)

and

Analysis  (a) The mass flow rate of the steam is

(b) There is only one inlet and one exit, and thus . Then the exit velocity is determined from

(c) We take the turbine as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Then the power output of the turbine is determined by substituting to be

6-169 EES Problem 6-168 is reconsidered. The effects of turbine exit area and turbine exit pressure on the exit velocity and power output of the turbine as the exit pressure varies from 10 kPa to 50 kPa (with the same quality), and the exit area to varies from 1000 cm2 to 3000 cm2 is to be investigated. The exit velocity and the power output are to be plotted against the exit pressure for the exit areas of 1000, 2000, and 3000 cm2.

Analysis The problem is solved using EES, and the results are tabulated and plotted below.

Fluid$='Steam_IAPWS'

A[1]=150 [cm^2]

T[1]=550 [C]

P[1]=10000 [kPa]

Vel[1]= 60 [m/s]

A[2]=1400 [cm^2]

P[2]=25 [kPa]

q_out = 30 [kJ/kg]

m_dot = A[1]*Vel[1]/v[1]*convert(cm^2,m^2)

v[1]=volume(Fluid$, T=T[1], P=P[1]) "specific volume of steam at state 1"

Vel[2]=m_dot*v[2]/(A[2]*convert(cm^2,m^2))

v[2]=volume(Fluid$, x=0.95, P=P[2]) "specific volume of steam at state 2"

T[2]=temperature(Fluid$, P=P[2], v=v[2]) "[C]" "not required, but good to know"

"[conservation of Energy for steady-flow:"

"Ein_dot - Eout_dot = DeltaE_dot"  "For steady-flow, DeltaE_dot = 0"

DELTAE_dot=0 "[kW]"

"For the turbine as the control volume, neglecting the PE of each flow steam:"

E_dot_in=E_dot_out

h[1]=enthalpy(Fluid$,T=T[1], P=P[1])

E_dot_in=m_dot*(h[1]+ Vel[1]^2/2*Convert(m^2/s^2, kJ/kg))

h[2]=enthalpy(Fluid$,x=0.95, P=P[2])

E_dot_out=m_dot*(h[2]+ Vel[2]^2/2*Convert(m^2/s^2, kJ/kg))+ m_dot *q_out+ W_dot_out

Power=W_dot_out

Q_dot_out=m_dot*q_out

| Power [kW] | P2 [kPa] | Vel2 [m/s] |
| --- | --- | --- |
| -54208 | 10 | 2513 |
| -14781 | 14.44 | 1778 |
| 750.2 | 18.89 | 1382 |
| 8428 | 23.33 | 1134 |
| 12770 | 27.78 | 962.6 |
| 15452 | 32.22 | 837.6 |
| 17217 | 36.67 | 742.1 |
| 18432 | 41.11 | 666.7 |
| 19299 | 45.56 | 605.6 |
| 19935 | 50 | 555 |

6-170E Refrigerant-134a is compressed steadily by a compressor. The mass flow rate of the refrigerant and the exit temperature are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 The device is adiabatic and thus heat transfer is negligible.

Properties From the refrigerant tables (Tables A-11E through A-13E)

Analysis  (a) The mass flow rate of refrigerant is

(b) There is only one inlet and one exit, and thus . We take the compressor as the system, which is a control volume since mass crosses the boundary. The energy balance for this steady-flow system can be expressed in the rate form as

Substituting,

Then the exit temperature becomes

6-171 Air is preheated by the exhaust gases of a gas turbine in a regenerator. For a specified heat transfer rate, the exit temperature of air and the mass flow rate of exhaust gases are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time. 2 Kinetic and potential energy changes are negligible. 3 There are no work interactions. 4 Heat loss from the regenerator to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid. 5 Exhaust gases can be treated as air. 6 Air is an ideal gas with variable specific heats.

Properties The gas constant of air is 0.287 kPa.m3/kg.K (Table A-1). The enthalpies of air are (Table A-21)

Analysis (a) We take the air side of the heat exchanger as the system, which is a control volume since mass crosses the boundary. There is only one inlet and one exit, and thus . The energy balance for this steady-flow system can be expressed in the rate form as

Substituting,

h2  =  794.71  kJ/kg

Then from Table A-21 we read

T2  =  775.1 K

(b)  Treating the exhaust gases as an ideal gas, the mass flow rate of the exhaust gases is determined from the steady-flow energy relation applied only to the exhaust gases,

It yields

6-172 Water is to be heated steadily from 20°C to 55°C by an electrical resistor inside an insulated pipe.  The power rating of the resistance heater and the average velocity of the water are to be determined.

Assumptions 1 This is a steady-flow process since there is no change with time at any point within the system and thus . 2 Water is an incompressible substance with constant specific heats. 3 The kinetic and potential energy changes are negligible, . 4 The pipe is insulated and thus the heat losses are negligible.

Properties The density and specific heat of water at room temperature are ( = 1000 kg/m3 and  c = 4.18 kJ/kg·°C  (Table A-3).

Analysis (a) We take the pipe as the system. This is a control volume since mass crosses the system boundary during the process.  Also, there is only one inlet and one exit and thus . The energy balance for this steady-flow system can be expressed in the rate form as

The mass flow rate of water through the pipe is

Therefore,

(b)  The average velocity of water through the pipe is determined from

6-173 CD EES An insulated cylinder equipped with an external spring initially contains air. The tank is connected to a supply line, and air is allowed to enter the cylinder until its volume doubles. The mass of the air that entered and the final temperature in the cylinder are to be determined.

Assumptions 1 This is an unsteady process since the conditions within the device are changing during the process, but it can be analyzed as a uniform-flow process since the state of fluid at the inlet remains constant.  2 The expansion process is quasi-equilibrium.  3 Kinetic and potential energies are negligible. 4 The spring is a linear spring. 5 The device is insulated and thus heat transfer is negligible. 6 Air is an ideal gas with constant specific heats.

Properties The gas constant of air is R = 0.287 kJ/kg·K (Table A-1). The specific heats of air at room temperature are cv = 0.718 and cp = 1.005 kJ/kg·K (Table A-2a). Also, u = cvT  and h = cpT.

Analysis We take the cylinder as the system, which is a control volume since mass crosses the boundary. Noting that the microscopic energies of flowing and nonflowing fluids are represented by enthalpy h and internal energy u, respectively, the mass and energy balances for this uniform-flow system can be expressed as

Mass balance:

Energy balance:

Combining the two relations,

or,

The initial and the final masses in the tank are

Then from the mass balance becomes

The spring is a linear spring, and thus the boundary work for this process can be determined from

Substituting into the energy balance, the final temperature of air T2 is determined to be

It yields		T2  =  344.1 K

Thus,

and		mi  =  m2  -  m1  =  2.430  -  0.472  =  1.96 kg

6-174E … 6-178  Design and Essay Problems

((

# Text boxes

Heat exchanger

Exh. gas

400(C

Q

Water

15(C

Warm

air

34(C

Room

24(C

Cold

air

5(C

85(F

73(F

60(F

Water

Steam

85(F

70(C

Water

20(C

4.5 kg/s

Oil

170(C

10 kg/s

Exhaust gases

1.1 kg/s, 95(C

Air

95 kPa

20(C

0.8 m3/s

Cold Water

15(C

0.60 kg/s

Hot water

100(C

3 kg/s

40(C

Hot oil

150(C

2 kg/s

Cold

water

22(C

1.5 kg/s

40(C

Cold Water

20(C

Hot Glycol

80(C

2 kg/s

Steam

10 psia

200(F

0.1 lbm/s

3

1

2

100 kPa

60(C

Water

100 kPa

50(C

10 kg/s

Steam

100 kPa

160(C

0.2 kg/s

Water

Steam

20 kPa

2

1

4

3

Steam

AIR

2

1

4

3

R-134a

Water

Cold plate

Water

inlet

3

2

1

Water

50(C

200 kg/s

Water

90(C

30 kg/s

3

1

2

10 psia

120(F

Water

10 psia

100(F

2 lbm/s

·

·

T1 = 12(C

m1 = 2m2

T2 = 60(C

R-134a

(P = 1 MPa)

T3,  x3

·

·

Sat. vapor

m2 = m1

T1 = 50(F

H2O

(P = 50 psia)

T3, x3

Air

30(C

0.6 m3/min

2

1

qin

800 kPa

Sat. Liq.

Water

800 kPa

sat. vap.

1

2

·

·

Throttling valve

100 kPa

120(C

Steam

2 MPa

I

100 kPa

100(C

1 MPa

200(C

1 kg/s

II

120 kPa

20°C

10 L/s

1 MPa

300°C

Compressor

15 psia

100°F

150 psia

700°F

5 lbm/s

Turbine

100 kPa

200°C

10 m/s

1 MPa

600°C

30 m/s

Turbine

100 kPa

CO2

5 MPa

100(C

Air

P2 = 14.7 psia

P1 = 200 psia

T1 = 90(F

H2O

P2 = 6 MPa

P1 = 8 MPa

T1 = 500(C

R-134a

T2 = -20(C

P1 = 0.8 MPa

T1 = 25(C

T2 = 20(C

m2

T1 = 80(C

m1 = 0.5 kg/s

H2O

(P = 250 kPa)

T3 = 42(C

1

2

CO2

Q

·

W

P1 = 120 kPa

T1 = 310 K

P2 = 700 kPa

T2 = 430 K

·

He

90 kg/min

12.5 MPa

550(C

20 kg/s

STEAM

20 kg/s

R-134a

-12°C

50°C

Sat. liquid

60 psia

250°F

50 ft3/s

500 psia

800°F

Turbine

100 kPa

20°C

30 m/s

1.8 MPa

400°C

Compressor

100 kPa

150°C

1 MPa

500°C

40 m/s

Turbine

250 kW

P2 = 150 kPa

V2 = 150 m/s

A1 = 60 cm2

P1 = 900 kPa

T1 = 450(C

V1 = 80 m/s

ARGON

2

1

300(C

200 kPa

Q

STEAM

400(C

800 kPa

10 m/s

2 kJ/s

2

1

R-134a

2

1

N2

P2 = 10 kPa

x2 = 0.92

V2 = 50 m/s

P1 = 10 MPa

T1 = 450(C

V1 = 80 m/s

·

STEAM

m = 12 kg/s

2

1

R-134a

2

1

AIR

2

1

AIR

H2O

·

W

P1 = 3 MPa

T1 = 400(C

V1 = 40 m/s

P2 = 2.5 MPa

V2 = 300 m/s

Steam

1

H2O

2

1

120 kJ/s

2

1

Steam

P1 = 300 kPa

T1 = 200(C

V1 = 30 m/s

A1 = 80 cm2

P2 = 100 kPa

V2 = 180 m/s

AIR

25 m/s

18 kg/min

Air

300 kPa

77(C

AIR

120 kPa

20°C

1 MPa

300°C

Compressor

50 psia

Water

10 psia

Q

H2O

Sat. vapor

P = 30 psia

7 MPa

65(C

Steam

6 MPa, 450(C

80 m/s

180 kPa

40(C

## Q

R-134a

200 kPa

20(C

5 m/s

AIR

250 psia

645(F

300 psia

700(F

80 ft/s

AIR

V2 = 180 m/s

V1 = 40 m/s

A1 = 90 cm2

V2

V1

700 kPa

Water

70 kPa

15(C

H2O

2

200 kPa

90(C

100 kPa

20(C

500 m/s

Steam, 200 psia

600(F, 59 ft/s

V1 = 1 m3

(1 =1.18 kg/m3

Smoking Lounge

15 smokers

30 L/s person

House

200 m2

0.35 ACH

2 MPa

sat. vap.

180 W

25(C

40(C

1

Air

30(C

0.6 m3/s

2

1

Water

55(F

4 lbm/s

2

180(F

2

1

Air

32(C

0.8 L/s

1

Water

90(C

0.8 m/s

2

88(C

5(6(8 m3

We

200 W

200 kJ/min

We

300 W

300 W

T2 = 47(C

A2 = 60 cm2

P1 = 100 kPa

T1 = 22(C

We = 1200 W

·

120 kg/min

AIR

##### Q

·

qout

1200 kPa

80(C

R134a

1200 kPa

sat. liq.

qin

500 psia,

sat. liq.

Water

500 psia

600(F

1 MPa

300(C

STEAM

##### Q

·

800 kPa

250(C

D1

200 kPa

200(C

V1

D2

150 kPa

150(C

V2

Steam

5 MPa

350(C

Water

5 MPa, sat. liq.

10 kg/s

Qin

.

100 kPa

30(C

Air

100 kPa, 15(C

0.3 m3/s

We,in

.

14.7 psia

80(F

Air

14.7 psia, 70(F

0.5 ft3/s

We,in

.

AIR

dr

Air

4000 kPa 20(C, 0.5 m3

Helium

Initially

evacuated

200 kPa, 120(C

8 L

Evacuated

100 kPa

17(C

initially evacuated

Air

Pi = 600 kPa

Ti = 22(C

V1 = 2 m3

P1 = 100 kPa

T1 = 22(C

Q

·

1 MPa

100(C

0.2 m3

R-134a

R-134a

Oxygen

2000 psia 80(F, 30 ft3

Liquid R-134a

5 kg

24(C

A-C line

20 psia 70(F

2 ft3

120 psia, 100(F

Air

(P = 200 kPa)

m1 = 10 kg

H2O

Pi = 0.5 MPa

Ti = 350(C

1.2 MPa

36(C

R-134a

0.12 m3

1 MPa

Sat. vapor

R-134a

Q

H2O

Sat. liquid

T = 200(C

V = 0.3 m3

##### Q

R-134a

Sat. vapor

P = 800 kPa

V = 0.12 m3

Q

R-134a

Sat. vapor

P = 100 psia

V = 4 ft3

Q

STEAM

2 MPa

Q

r

R

He

0.08 m3

2 MPa

80(C

AIR

60 ft3

75 psia

120(F

We

AIR

300 kPa

0.2 m3

20(C

R-134a

0.8 m3

1.2 MPa

120(C

z

D

D0

Steam

0.6 kg

0.1 m3

800 kPa

Steam

5 MPa

500(C

Q

D1

200 kPa

50(C

V1

D2

150 kPa

40(C

V2

Air

q

0.5 hp

85 m3/min

Water

150(C

Heater

Steam

Cold water

20(C

Water

Heater

Steam

Cold water

20(C

R-134a

0.4 kg, 1 L

25(C

Air

34(F

Egg

0.14 lbm

Water bath

55(C

Water bath

50(C

350(C

Aluminum wire

10 m/min

350(C

Copper wire

10 m/min

Cold Water

25(C

Steam

40(C

35(C

Compressor

1 MPa

300°C

120 kPa

20°C

Turbine

1.6 MPa

350°C

16 kg/s

30°C

sat. vap.

Heat

50 psia

70(F

N2

100 psia

120(F

20(C

water

15(C

0.1 L/s

We,in

.

1000 kPa

D=0.1 m

Water

1400 kPa, 350(C

D=0.15 m, 10 m/s

1.4 MPa

36°C

1.6 MPa

40°C

50 m/s

1.4 MPa

36°C

H2O

1

2

30 kJ/kg

R-134a

2

1

AIR

Exhaust Gases

3

4

1

2

We

·

30 L/min

D = 5 cm

WATER

Air

P = 200 kPa

T1 = 22(C

V1 = 0.2 m3

Pi = 0.8 MPa

Ti = 22(C

Fspring

2

1

CO2